## Slide 1: Work Health and Safety Regulations 2012 (SA) Chapter 10 (Mines)
Mar 2021

## Slide 2: Disclaimer
IMPORTANT: The information in this presentation is of a general nature, and should not be relied upon as individual professional advice. If necessary, legal advice should be obtained from a legal practitioner with expertise in the field of Work Health and Safety law (SA).
Although every effort has been made to ensure that the information in this presentation is complete, current and accurate, the Mining and Quarrying Occupational Health and Safety Committee, any agent, author, contributor or the South Australian Government, does not guarantee that it is so, and the Committee accepts no responsibility for any loss, damage or personal injury that may result from the use of any material which is not complete, current and accurate.
Users should always verify historical material by making and relying upon their own separate inquiries prior to making any important decisions or taking any action on the basis of this information.

## Slide 3: Creative Commons
This creative commons licence allows you to copy, communicate and adapt the work for non-commercial purposes, as long as you attribute the work to Mining and Quarrying Occupational Health and Safety Committee and abide by all the other licence terms therein.
ISBN 978-1-925361-43-8

## Slide 4: Introduction
New Work Health and Safety (WHS) “Mines” Regulations (Chapter 10) came into effect in South Australia on 1 January 2014.
The Mines Regulations are part of the broader WHS Regulations 2012 (SA) and operate in addition to the obligations that apply to all workplaces.
The Mines Regulations contain requirements that are specific to mining and quarrying activities.
Most of these requirements will be familiar to the mining and quarrying industry and existing safety arrangements will in many cases comply with the new requirements.
The most obvious difference to the previous regulations is the requirement for a documented Safety Management System.
This requirement for a Safety Management System provides the basis for managing all risks to health and safety associated with mining and quarrying.

## Slide 5: Introduction
The Safety Management System describes such things as: policies, management structures, contractor management arrangements and importantly hazard and risk control measures, encompassing principal mining hazards.
The regulations recognise that not all mines and quarries are the same and as such the detail contained in the management system will depend on the nature and complexity of the operation.

## Slide 6: Mines Regulations - Key Elements
Mine & Mining Operations;
Mine Holder / Mine Operator – primary duty holder;
Mine Manager and competencies;
Managing risks;
  control of risk
  safety management system
  principal mining hazards
  operational controls – all mines and underground specific
  emergency management
  information instruction and training

## Slide 7: Mines Regulations - Key Elements
Mine survey plan;
Safety role for workers;
Mines specific notifications;
Mine record; and
National Mine Safety Database (NMSD) quarterly reporting.

## Slide 8: A Mine
The WHS Regulations 2012 (SA), define a mine as:
  Any workplace at which mining operations are carried out; or
  A tourist mine; and
  Any fixtures, fittings, plant or structures at the place that are used or were formerly used for mining operations.
A tourist mine is defined as a workplace:
  used only for tourism purposes but at which mining operations were formerly carried out; and
  at which there is a principal mining hazard that was present at the workplace when the mining operations were carried out.
An underground mine means that part of a mine that is beneath the surface of the earth and includes plant and structures that extend continuously from the surface into that part of the mine.

## Slide 9: Mining Operations
  Mining operations include activities carried out for the purpose of:
  Extracting minerals from, or injecting minerals into the ground, and
  Exploring for minerals by mechanical means that disturb the ground, and
  Activities carried out in connection with mining activities at a site, or at a site adjoining or in the vicinity of a site, at which the mining activities are carried out.
  Mining activities include:
  Handling, storing, preparing or processing extracted materials;
  Constructing a site or at a site adjoining where a mining activity is carried out;
  Activities associated with decommissioning, making safe or closure of an extraction site or exploration site; and
  Educational and tourist activities carried out at a site, or at a site adjoining or in the vicinity of a site, at which the mining activities are carried out.
Notes: The WHS Mines Regulations now apply to activities carried out in connection with and adjoining to or in the vicinity of mining activities at a site, as well as construction activities relating to existing or proposed new mining operations. This means that this legislation will have jurisdiction over some construction sites prior to any mining taking place, which will have a significant impact on greenfield sites and brownfield expansion projects in relation to how safety is administered.
Mining operations do not include:
  an activity carried out in relation to the extraction of minerals on private land for the private and non-commercial use of the owner of the land;
  fossicking;
  any activity where the extraction of minerals is incidental to the activity. E.g civil works such as tunnelling to create a road.

## Slide 10: Mining Operations
  Mining operations do not include:
  An activity carried out in relation to the extraction of minerals on private land for the private, and non-commercial use of the owner of the land;
  Fossicking; and
  Any activity where the extraction of minerals is incidental to the activity. Example - Civil works such as tunnelling to create a road.
Notes: The WHS Mines Regulations now apply to activities carried out in connection with and adjoining to or in the vicinity of mining activities at a site, as well as construction activities relating to existing or proposed new mining operations. This means that this legislation will have jurisdiction over some construction sites prior to any mining taking place, which will have a significant impact on greenfield sites and brownfield expansion projects in relation to how safety is administered.
Mining operations do not include:
  an activity carried out in relation to the extraction of minerals on private land for the private and non-commercial use of the owner of the land;
  fossicking;
  any activity where the extraction of minerals is incidental to the activity. E.g civil works such as tunnelling to create a road.

## Slide 11: Mine Holder / Mine Operator
The Mine Holder of a mine:
Is the Mine Operator unless they appoint another PCBU to be the Mine Operator; and
The PCBU with control over a right or entitlement to carry out mining operations at the mine (primary duty holder).
Notes: The primary duty holder under the WHS Mines regs is the ‘mine operator’, which will be the ‘mine holder’ unless it appoints another person as the mine operator. The concept of a ‘person or business conducting a business or undertaking’ (PCBU) is retained in the definition of ‘mine holder’ which also includes a person with control over a right or entitlement to carry out mining activities or preparation or processing of extracted materials in connection with mining activities or at an adjoining site or in the vicinity of the mining activities at the site.
Worker representatives
WHS ACT
14—Duties not transferrable
A duty cannot be transferred to another person.
15—Person may have more than one duty
A person can have more than one duty by virtue of being in more than one class of duty holder.
16—More than one person can have a duty
More than one person can concurrently have the same duty.
Each duty holder must comply with that duty to the standard required by this Act even if another duty holder has the same duty.
If more than one person has a duty for the same matter, each person—
  retains responsibility for the person's duty in relation to the matter; and
  must discharge the person's duty to the extent to which the person has the capacity to influence and control the matter or would have had that capacity but for an agreement or arrangement purporting to limit or remove that capacity.
17—Management of risks
A duty imposed on a person to ensure health and safety requires the person—
  to eliminate risks to health and safety, so far as is reasonably practicable; and
  if it is not reasonably practicable to eliminate risks to health and safety, to minimise those risks so far as is reasonably practicable.
A person must comply with subsection (1) to the extent to which the person has the capacity to influence and control the matter or would have that capacity but for an agreement or arrangement purporting to limit or remove that capacity.
R625 The mine holder must, on request, provide information to the mine operator of an adjoining mine about conditions or activities (current/proposed) that may pose a risk to health and safety of persons at the adjoining mine

## Slide 12: Mine Operator Appointment
The Mine Holder of a mine, may only appoint a person to be the Mine Operator if:
The person is conducting a business or undertaking; and
Is appointed in accordance with R615 to carry out mining operations at the mine on behalf of the Mine Holder; and
The Mine Holder authorises the person to have management or control of the mine and to discharge the duties of a Mine Operator under the Act & Regulations.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 13: Mine Operator Notification
Notification of the Mine Operator (as mine holder or appointed) must be given to regulator before mining operations commence.
Notification must be:
In writing; and
Made in the manner and form required by the regulator.
SafeWork SA has provided a form which can be downloaded from their website:
Mine Holder or Mine Operator – Appointment and notification form.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 14: Mine Manager Appointment
A mine operator must ensure:
A competent person is appointed to be Mine Manager of a mine where mining operations are carried out; and
The Mine Manager holds the relevant competencies (general / prescribed) requirements to be a Mine Manager.
Note:
This does not apply in respect of mining operations carried out at a tourist mine, an exploration site or a precious stones field under the Opal Mining Act 1995.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 15: Mine Manager Appointment
A Mine Operator who is competent to be a Mine Manager in relation to the mine, may be appointed as Mine Manager.
However, a Mine Operator must not, unless permitted to do so in accordance with a determination by the regulator, appoint a Mine Manager of a mine, if the mine manager is a also a mine manager of a another mine.
Note:
There is nothing preventing more than 1 person being appointed as a mine manager to cover temporary absences of the mine manager.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 16: Mine Manager Competencies
Underground Mine or Quarry less than 20 workers
General competency requirements only. No prescribed experience or qualifications defined.
Underground Mine or Quarry with 20 or more workers
General competency requirements; and
Prescribed experience and qualifications.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 17: Mine Manager Competencies
General competencies – all Mine Managers
A Mine Operator, in appointing a person to be a manager of a underground mine or quarry, must be satisfied that the person:
Has the relevant training, qualifications, experience, knowledge and skills to manage and supervise the mining operations carried out at the mine; and
Has knowledge of the requirements of the WHS Act 2012 (SA) and the WHS Regulations 2012 (SA), particularly Chapter 10; and
Is capable of managing hazards at the mine.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 18: Mine Manager Competencies
General competencies – all Mine Managers
Mine Operators, in satisfying themselves that a person has knowledge of the WHS Act and the WHS Regulations (including Chapter 10):
People that have previously passed the mining law exam for their mine/quarry manager certification as having sufficient knowledge; or
Must individually assess any person who has not passed this exam to determine if they have sufficient knowledge.
For example, a Mine Operator develops an assessment module/adopt an industry module on WHS legislation.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 19: Mine Manager Competencies
Prescribed Competencies – 20 or more workers
A Mine Operator, in appointing a person to be a Mine Manager of an underground mine or quarry with 20 or workers, must be satisfied that the person:
Has the general competency requirements to be a Mine Manager; and
Meets any applicable prescribed competency requirements (experience and qualifications) to be a Mine Manager.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 20: Mine Manager Competencies
Experience - Quarry with 20 or more workers
The person to be appointed as a Mine Manager must have at least:
3 years practical experience in quarrying, during which the person had:
  1 year quarrying operational experience; and
  experience supervising quarry operations.
Qualifications - Quarry with 20 or more workers
The person to be appointed as a Mine Manager:
Holds a degree in mining engineering or diploma in surface operations management from a university or tertiary institution in Australia; or
An equivalent institution as determined by the regulator.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 21: Mine Manager Competencies
Experience - Underground with 20 or more workers
The person to be appointed as a Mine Manager has at least:
5 years working at a mine; and
At least 3 of those years, spent working at an underground mine during which the person had:
  2 years underground mining operational experience; and
  experience supervising underground mining operations.
Qualifications - Underground with 20 or more workers
The person to be appointed as a Mine Manager:
Holds a degree or diploma in mining engineering from a university or tertiary institution in Australia; or
An equivalent institution as determined by the regulator.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 22: Calculating the Number of Workers
The regulators position on calculating the number of workers at a mine or quarry for determining the applicable Mine Manager competencies is the following:
The number of workers in a 24 hour period under a mine’s normal operations, including contractors.
Note:
During shutdowns and major construction projects, any additional workers engaged in this period are not included in the calculation of number of workers.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 23: Calculating the Number of Workers
Additionally, a Mine Operator, if they choose, can divide the mine site into operational areas, such as:
Processing;
Surface mining;
Underground mining;
Concrete batching plants;
Maintenance workshops; and
Waste transfer stations etc.
The Mine Operator can then calculate the number of workers within those activities and appoint a manager as required.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 24: Mine Manager Records
A Mine Operator must ensure a record is kept:
Of the appointment of each Mine Manager to a mine;
Of any information provided to the Mine Operator by a Mine Manager, in satisfaction of the mine managers competency requirements; and
For the duration of the person's appointment as a Mine Manager, and for at least 2 years after the person ceases to be a Mine Manager at the mine.
Notes: Note: a form will is available on the SafeWork SA website to assist mines to comply with the appointment and notification requirements outlined above.
615 Appointment of mine operator
(1) An appointment of a person to be the mine operator of a mine must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and
  (c) include a signed statement that the person to be appointed as mine operator agrees to the appointment; and
  (d) specify:
    (i) the name and contact details of the mine operator, including postal and business addresses; and
    (ii) when the appointment takes effect; and
  (e) describe the location of the mine, including:
    (i) the boundaries of all extraction and exploration sites; and
    (ii) land title identification.
(2) The mine holder must give the mine operator all relevant information held by or under the control of the mine holder that may reasonably be required by the mine operator to discharge the duties imposed on the mine operator under the Act and these Regulations.
616 Notification of mine operator to regulator
(1) The mine holder of a mine must give notice to the regulator in accordance with this regulation.
(3) If the mine holder of a mine is not the mine operator, the mine holder must give the regulator notice of the appointment of the mine operator of the mine.
(4) A notice under subregulation (3) must:
  (a) be in writing; and
  (b) be made in the manner and form required by the regulator; and

## Slide 25: Control of Risk
A PCBU at a mine, must manage risks to health and safety associated with mining operations, and in doing so must ensure a risk assessment is conducted by a competent person.
In conducting a risk assessment, the person must have regard to:
The nature of the hazard; and
The likelihood of the hazard affecting the health or safety of a person; and
The severity of the potential health and safety consequences.
Notes: WHS Regs Chapter 10, Part 2, Div 3, Specific control measures – all mines,
630 – Communication between outgoing and incoming shifts,
631 – Movement of mobile plant,
632 – Prohibited uses, detailed in schedule 20
633 – Closure, suspension or abandonment,
634 – Minimum age to work at a mine

## Slide 26: Control of Risk
A PCBU at a mine must review, and as necessary, revise control measures implemented to manage risks, if:
An audit of the effectiveness of the SMS for the mine indicates a deficiency in a control measure; or
A worker is moved from a hazard or assigned to different work in response to a recommendation contained in a health monitoring report; or
A notifiable incident or mining incident occurs; or
A health and safety representative requests a review of a control measure.

## Slide 27: Control of Risk
A Mine Operator who has reviewed a control measure under R38, in relation to notifiable incident or mining incidents must keep a record of certain reviews of control measures.
A record of the following must be kept:
Work health and safety issues arising form the incident;
Recommendations arising from consideration of the incident; and
Summary of any changes to the safety management system and any affected principal mining hazard management plan for the mine.

## Slide 28: Control of Risk
A PCBU at a mine other than the Mine Operator, who has reviewed a control measure under R38, in relation to notifiable incident or mining incidents, must keep a record of the following:
Work health and safety issues arising form the incident; and
Recommendations arising from consideration of the incident.

## Slide 29: Safety Management Systems for Mines
Under the WHS Regulations 2012 (SA), R.621 - Duty to Establish and Implement Safety Management System (SMS)
Safety Management System R.621
Comprehensive & integrated
Used as primary means of ensuring health & safety or workers & others
Documented readily available &
understandable
Contents as specified in 622
Maintained to ensure effectiveness
Mine operator must establish & implement an SMS
Reviewed at least every 3 years & sooner to remain effective
Sufficient to refer to a plan/ document if already addressed
Part of overall management system
Appropriate to nature & complexity of the mine

## Slide 30: Safety Management Systems for Mines
Under the WHS Regulations 2012 (SA), R.622 - Content of Safety Management System
Safety Management System
Emergency Plan
Ventilation Control Plan & Ventilation Plan
Specific Control Measures
Principal Mining Hazard Management Plans
Withdrawal situations
Health & Safety Policy
Mine Survey Plan
Risk Management
Notifications
Worker & Contractor Management
Performance Standards & Audit

## Slide 31: Principal Mining Hazards
Regulation 612 of the WHS Regulations 2012 (SA), defines a Principal Mining Hazard (PMH) as:
Any activity;
Process;
Procedure;
Plant;
Structure;
Substance;
Situation; or
Other circumstance relating to the carrying out of mining operations that has a reasonable potential to result in multiple deaths in a single incident or a series of recurring incidents.

## Slide 32: Principal Mining Hazards
As listed in the WHS Regulations 2012 (SA), a PMH can be in relation to, but not limited to, any of the following:
Ground or strata failure;
Inundation or inrush of any substance;
Mine shafts and winding operations;
Roads or other vehicle operating areas;
Air quality, dust and other airborne contaminants;
Fire or explosion;
Gas outbursts;
Spontaneous combustion; or
A hazard identified by the mine operator of a mine under R34.
Notes: Regulation 34,
A duty holder, in managing risks to health and safety, must identify reasonably foreseeable hazards that could give rise to risks to health and safety.

## Slide 33: Principal Mining Hazards
The mine operator must:
Identify all PMHs at the mine;
For each PMH identified, conduct a risk assessment that:
  involves a comprehensive and systematic investigation and analysis of all aspects of risk to health and safety associated with the PMH; and
  considers each PMH individually and cumulatively with other hazards at the mine.
Develop control measures;
Prepare a Principal Mining Hazard Management Plan (PMHMP) for each PMH at the mine, having regard to the matters set out in Schedule 19 (2 extracts of Schedule 19 are provided on the following slides); and
Ensure PMHMPs are reviewed and as necessary revised if a risk control measure specified in the plan is revised under regulations 38 or 618.
Notes: Regulation 34,
A duty holder, in managing risks to health and safety, must identify reasonably foreseeable hazards that could give rise to risks to health and safety.

## Slide 34: Schedule 19
Ground or strata instability
The local hydrogeological environment, including surface and ground water
The local geological structure
The geotechnical characteristics of the rocks and soil, including the effects of time, oxidation and water on rock support and stability;
Any natural or induced seismic activity;
The location and loadings from existing or proposed mine infrastructure such as waste dumps, tailings storage, haul roads and mine facilities;
Proposed and existing mining operations, including the nature and number of excavations, the number and size of permanent or temporary voids or openings, backfilling of mined areas and stopes, abutments, periodic weighting and windblast;
Any previously excavated or abandoned workings
Proposed blasting activities, including air blast
The following matters must be considered in developing the control measures to manage the risks of ground or strata instability

## Slide 35: Schedule 19
Air Quality, Dust and other Airborne Contaminants
The temperature and humidity of the air
The length of exposure, having regard to extended shifts and reduced recovery periods.
The level of oxygen, dust and other contaminants in the natural or supplied air of the mine
Types of dust and other chemical and biological contaminants likely to be in the air from both natural sources, including naturally occurring asbestos, and introduced sources
The following matters must be considered in developing the control measures to manage the risks of air quality, dust and other airborne contaminants

## Slide 36: Specific Control Measures – all mines
The Mine Operator must implement specific control measures at all mines including:
  Communication between outgoing and incoming shifts;
  Movement of mobile plant;
  Prohibited uses;
  Closure, suspension or abandonment of mine;
  Minimum age to work in mine; and
  Operational controls.
Notes: 630—Communication between outgoing and incoming shifts
The mine operator of a mine at which more than 1 shift is worked each day must
implement a system that ensures that, as soon as practicable at the commencement of
each shift—
the supervisor of each outgoing shift provides a written report to the supervisor of the incoming shift, in relation to the state of the mine workings and plant and any other matters that relate to work health or safety; and
the supervisor of the incoming shift communicates the content of the report to the workers on the incoming shift.
631—Movement of mobile plant -
In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with the movement of mobile plant at the mine.
In managing risks to health and safety associated with the movement of mobile plant at the mine, the mine operator must have regard to all relevant matters including the following:
  (a) the design, layout, construction and maintenance of all roads and other areas at the mine used by mobile plant;
  (b) interactions between mobile plant, especially between large and small mobile plant;
  (c) interactions between mobile plant and fixed plant or structures;
  (d) interactions between mobile plant and pedestrians (including the use of pre-movement warnings for mobile plant in mine workings);
  (e) the operation of remotely controlled mobile plant;
  (f) the maintenance, testing and inspection of brakes, steering, lights and other safety features of the mobile plant.
Note—
Division 7 of Chapter 5 Part 1 includes requirements relating to mobile plant in all workplaces.
632—Prohibited uses
The mine operator of a mine must take all reasonable steps to ensure an item or substance specified in Schedule 20, column 1 is not used in a place or for a purpose that is prohibited or restricted as set out in Schedule 20, column 2 opposite that item or substance.
634—Minimum age to work in mine
The mine operator of a mine must take all reasonable steps to ensure that—
  (a) a person under the age of 16 years is not engaged to carry out work in any open cut workings or in an underground mine; and
  (b) a person under the age of 18 years is not engaged to carry out work in an underground mine, unless the person is over the age of 16 years and is an apprentice or trainee under direct supervision in relation to the work.
640—Fatigue
In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with worker fatigue.
641—Alcohol and drugs
(1) In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with the consumption of alcohol by workers.
(2) In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with the use of drugs by workers.
50—Monitoring airborne contaminant levels
(1) A person conducting a business or undertaking at a workplace must ensure that air
monitoring is carried out to determine the airborne concentration of a substance or
mixture at the workplace to which an exposure standard applies if—
(a) the person is not certain on reasonable grounds whether or not the airborne
concentration of the substance or mixture at the workplace exceeds the
relevant exposure standard; or
(b) monitoring is necessary to determine whether there is a risk to health.
(2) A person conducting a business or undertaking at a workplace must ensure that the
results of air monitoring carried out under subregulation (1) are recorded, and kept for
30 years after the date the record is made.

## Slide 37: Specific Control Measures – all mines
Air quality and monitoring incudes:
  Temperature and moisture content of air;
  Exposure standards – compliance and monitoring;
  Air monitoring – use of devices and signage; and
  Requirements under WHS Regulation 50 (monitoring & record keeping).
Fitness for work includes:
  Fatigue; and
  Alcohol and drugs.
Notes: 630—Communication between outgoing and incoming shifts
The mine operator of a mine at which more than 1 shift is worked each day must
implement a system that ensures that, as soon as practicable at the commencement of
each shift—
the supervisor of each outgoing shift provides a written report to the supervisor of the incoming shift, in relation to the state of the mine workings and plant and any other matters that relate to work health or safety; and
the supervisor of the incoming shift communicates the content of the report to the workers on the incoming shift.
631—Movement of mobile plant -
In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with the movement of mobile plant at the mine.
In managing risks to health and safety associated with the movement of mobile plant at the mine, the mine operator must have regard to all relevant matters including the following:
  (a) the design, layout, construction and maintenance of all roads and other areas at the mine used by mobile plant;
  (b) interactions between mobile plant, especially between large and small mobile plant;
  (c) interactions between mobile plant and fixed plant or structures;
  (d) interactions between mobile plant and pedestrians (including the use of pre-movement warnings for mobile plant in mine workings);
  (e) the operation of remotely controlled mobile plant;
  (f) the maintenance, testing and inspection of brakes, steering, lights and other safety features of the mobile plant.
Note—
Division 7 of Chapter 5 Part 1 includes requirements relating to mobile plant in all workplaces.
632—Prohibited uses
The mine operator of a mine must take all reasonable steps to ensure an item or substance specified in Schedule 20, column 1 is not used in a place or for a purpose that is prohibited or restricted as set out in Schedule 20, column 2 opposite that item or substance.
634—Minimum age to work in mine
The mine operator of a mine must take all reasonable steps to ensure that—
  (a) a person under the age of 16 years is not engaged to carry out work in any open cut workings or in an underground mine; and
  (b) a person under the age of 18 years is not engaged to carry out work in an underground mine, unless the person is over the age of 16 years and is an apprentice or trainee under direct supervision in relation to the work.
640—Fatigue
In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with worker fatigue.
641—Alcohol and drugs
(1) In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with the consumption of alcohol by workers.
(2) In complying with regulation 617, the mine operator of a mine must manage risks to health and safety associated with the use of drugs by workers.
50—Monitoring airborne contaminant levels
(1) A person conducting a business or undertaking at a workplace must ensure that air
monitoring is carried out to determine the airborne concentration of a substance or
mixture at the workplace to which an exposure standard applies if—
(a) the person is not certain on reasonable grounds whether or not the airborne
concentration of the substance or mixture at the workplace exceeds the
relevant exposure standard; or
(b) monitoring is necessary to determine whether there is a risk to health.
(2) A person conducting a business or undertaking at a workplace must ensure that the
results of air monitoring carried out under subregulation (1) are recorded, and kept for
30 years after the date the record is made.

## Slide 38: Emergency Management
These requirements are in addition to the requirements under WHS Regulation R43(1).
Specific requirements for all mines:
  Duty to prepare emergency plan;
  Consultation in preparation of emergency plan;
  Implementation of emergency plan;
  Copies to be kept and provided;
  Resources for emergency plan;
  Testing of emergency plan; and
  Review.
Notes: Division 4—Emergency plans
43—Duty to prepare, maintain and implement emergency plan
(1) A person conducting a business or undertaking at a workplace must ensure that an emergency plan is prepared for the workplace, that provides for the following:

## Slide 39: Emergency Management
Specific requirements for underground mines:
  Emergency exits (includes at least 2 trafficable exits);
  Safe escape and refuge;
  Signage for refuges;
  Self-rescuers; and
  Personal protective equipment in emergencies.
Notes: Division 4—Emergency plans
43—Duty to prepare, maintain and implement emergency plan
(1) A person conducting a business or undertaking at a workplace must ensure that an emergency plan is prepared for the workplace, that provides for the following:

## Slide 40: Emergency Management
When developing an Emergency management plan, the following items listed in Schedule 22 of the WHS regulations are required to be included:
  Site and hazard detail;
  Command structure and site personnel;
  Notifications;
  Resources and equipment; and
  Procedures.

## Slide 41: Information, Training & Instruction
In addition to the requirements under WHS Regulation R39, the mine operator has a duty to and provide information, training and instruction to workers regarding:
  All hazards associated with their work;
  Risk control measures, including fatigue & the consumption of alcohol and drugs;
  The safety management system;
  The emergency plan; and
  The safety role for workers in relation to principal mining hazards.

## Slide 42: Information, Training & Instruction
The mine operator has a duty to:
  Develop and implement induction procedures for workers and contractors at the mine;
  Provide information & instruction to visitors to ensure they are:
  informed about risks
  instructed in health & safety precautions and emergency procedures
  Review and if necessary revise any information, training and instruction; and
  Keep records of training.

## Slide 43: Health Monitoring
The Mine Operator of a mine must ensure that health monitoring is provided to a worker of a mine where there is:
A significant risk of an adverse effect on the worker's health because of the worker's exposure to a hazard associated with mining; and
  Valid techniques are available to detect that effect on the worker's health.

## Slide 44: Health Monitoring
In carrying out health monitoring, a PCBU / Mine Operator must:
Inform the worker of health monitoring;
Engage a registered medical practitioner experienced in health monitoring to supervise / carry out the monitoring;
Pay all associated cost;
Provide registered medical practitioner with information;
Ensure health monitoring report meets WHS regulatory requirements;
Obtain / provide a copy of the report to the mine operator and worker, and in specific circumstances, the regulator; and
Keep health monitoring records.

## Slide 45: Safety Role for Workers
Regulation 675Q of the WHS Regulation 2012 (SA), “Safety role for workers in relation to principal mining hazards” states:
The Mine Operator of a mine must implement a safety role for the workers at the mine that enables them to contribute to:
  the identification of principal mining hazards that are relevant to the work that the workers are or will be carrying out;
  the consideration of control measures for risks associated with principal mining hazards at the mine; and
  the conduct of a review of a PMH management plan.
The Mine Operator of a mine must ensure the safety role for workers is documented in the SMS and communicated to all workers.
  A simple way of achieving this is to include the “safety role” in relation to principal mining hazards, into the workers position description or workplace induction.

## Slide 46: Consultation
For the purposes of Section 49 of the WHS Act 2012 (SA), the mine operator must consult with workers in relation to:
  The development, implementation and review of the safety management system;
  Risk assessments for PMH management plans;
  Preparing, testing and review of the emergency plan;
  Implementation of the workers’ safety role; and
  Strategies relating to the consumption of alcohol or drugs and worker fatigue.

## Slide 47: Contractor Management
If a contractor is working or likely to work at a mine or quarry, the Safety Management System (SMS) document for the mine or quarry, must set out the control measures associated with the contractor’s work, including:
  How the contractor's work management system will be integrated with the SMS of the mine/quarry;
  The process for assessing the contractor’s health and safety policies and procedures (including competency requirements) and integrating them into the SMS; and
  The arrangements for monitoring and evaluating compliance by the contractor with the health and safety requirements of the safety management system.

## Slide 48: Incident Notification
In addition to the notification requirements under Section 38 of the WHS Act 2012 (SA), mine operators also have a duty to notify SafeWork SA of certain incidents including:
  A high potential incident – relates to incidents under Section 37 of the Act, but expanded to include where a person could have been in the vicinity in usual circumstances;
  Illness or injury that requires medical treatment as defined in Schedule 24 of the Regulations.
Schedule 23 of the WHS Regulations 2012 (SA), outlines the information to be included in the notification of a mining incident including details relating to the person injured, incident and consequences of incident.
Note:
A “Dangerous Incident” as described in Section 38 of the Act, now includes unplanned loss of control of heavy earthmoving machinery at a mine or quarry.

## Slide 49: Mine Survey Plan
The Mine Operator of a mine must ensure:
A detailed survey plan of the mine is prepared by a competent person; and
Take all reasonable steps to obtain historical mine surveys.
Note: a competent person means:
A person who has acquired through training, qualification or experience the knowledge and skills to carry out the task. (WHS Regulation 5)

## Slide 50: Mine Survey Plan
The plan must show the following (if present at the mine):
The workings of the mine, including disused workings and bore holes;
The location of electrical installations;
The location of telephones and other fixed plant associated with the radio and telecommunications systems;
Water dams and tailings dams, natural features surrounding the mine;
Places for the storage of hydrocarbons or explosives;
Points of entry and exit, including emergency exits; and
Refuges (in an underground mine).

## Slide 51: Mine Survey Plan
The mine operator of a mine must review and as necessary revise the mine survey plan:
  If it no longer accurately reflects the workings or proposed workings; or
  If there are reasonable grounds to believe that it’s not accurate; or
  At least once every 12 months; and
  File any relevant copies of mine surveys on suspension, closure or surrender of a mine.

## Slide 52: Mine Record
The mine operator of a mine must keep a mine record for the mine, and must contain a record of any notice issued in relation to enforcement measures.
These notices relate to:
  An improvement notice;
  A prohibition notice; and
  A non disturbance notice.

## Slide 53: Mine Record
The mine record must also contain:
  A copy of any provisional improvement notice issued to the mine;
  A record of every notifiable incident to the regulator;
  A summary of all records from a review of certain control measures relating to a notifiable incident or a high potential incidents; and
  A shift report from each shift supervisor at the mine where there is more than 1 shift worked in any 24 hour period.

## Slide 54: Mine Record
Where there is more than 1 shift worked in any 24 hour period at the mine, the mine record must also contain:
  A copy of the shift change-over report from the out-going supervisor to the in-coming supervisor.
  The state of the mine workings;
  Any plant and any other matters that relate to work health or safety; and
  Evidence the report has been communicated by the in-coming supervisor to workers on the in-coming shift.

## Slide 55: Mine Record
The Mine Operator of a mine must:
Keep a record that forms part of the mine record for 7 years from the date the record was made.
Make the mine record for the mine available for inspection under the Act.
Ensure that the mine record for the mine is available to workers at the mine on request but shall only make available a summary of all notifable incidents.
The Mine Operator must not provide personal or medical information in relation to a worker without the worker's written consent unless the information is:
In a form that does not identify the worker; and
Could not reasonably be expected to lead to the identification of the worker.

## Slide 56: Mine Quarterly Reporting
Regulation 675W of the WHS Regulations 2012 (SA), came into effect as of 1st January 2015. The Mine Operator of a mine must give the regulator a quarterly report. Note: At this time the information is to be recorded/retained on file and provided upon request.

## Slide 57: Further Information and Assistance
MAQOHSC has developed a free suite of WHS materials to assist mine or quarrying operators in meeting their WHS legislative obligations including Chapter 10 - Mines.
These include:
Presentations and guidance materials to assist stakeholders in understanding their WHS legislative requirements;
WHS templates, forms and registers to assist stakeholder in the development of a safety management system; and
Risk management tools to assist stakeholders in identifying, assessing and controlling risks to health and safety.

## Slide 58: Further Information and Assistance
Work Heath and Safety Legislation, Codes of Practice, fact sheets, guides and WHS materials, can be found at the following websites:
MAQOHSC – www.maqohsc.sa.gov.au
SafeWork SA – www.safework.sa.gov.au
Safe Work Australia – www.safeworkaustralia.gov.au

## Slide 59: Further Information and Assistance
MAQOHSC is also available to provide guidance, onsite support and advice on WHS Matters.
To contact MAQOHSC, please visit our website at:
www.maqohsc.sa.gov.au and make a request for support.
Alternatively, if you would like to speak with someone directly, feel free to contact us on: (08) 8204 9842
Think Safety
Work Safely!