## Slide 1
Occupational Dust
Exposure and Management
November 2018

## Slide 2: The Mining and Quarrying Occupational Health and Safety Committee
The Mining and Quarrying Occupational Health and Safety Committee is a tripartite Committee established under the South Australian Occupational Health, Safety and Welfare Act 1986 (SA) and continues existence under the Work Health and Safety Act 2012 (SA).
The Committees mandate is to protect workers, promote best hygiene practices, support workplace health and safety and prevent injury, death and disease within the mining and quarrying sectors.
This workplace industry safety resource is developed and fully funded by the Mining and Quarrying Occupational Health and Safety Committee (MAQOHSC).

## Slide 3: Disclaimer
IMPORTANT: The information in this presentation is of a general nature, and should not be relied upon as individual professional advice. If necessary, legal advice should be obtained from a legal practitioner with expertise in the field of Work Health and Safety law in South Australia.
Although every effort has been made to ensure that the information in this presentation is complete, current and accurate, the Mining and Quarrying Occupational Health and Safety Committee, any agent, author, contributor or the South Australian Government, does not guarantee that it is so, and the Committee accepts no responsibility for any loss, damage or personal injury that may result from the use of any material which is not complete, current and accurate.
Users should always verify historical material by making and relying upon their own separate inquiries prior to making any important decisions or taking any action on the basis of this information.

## Slide 4: Overview
Dust Exposure
Respirable Dust
Silica
Respirable Crystalline Silica
How Silica Can Affect the Lungs
Onset of Silicosis
Contributing Factors
Dust Management
Legislative Requirements
Practicable Dust Control Measures
MAQOHSC

## Slide 5: Dust Exposure
Dust is a recognised hazard for workers in the mining and quarrying sector.
The generation of dust particles are a common occurrence associated with mining and quarrying activities.
Dust is generated by the breaking down of a solid mineral mass to a size where the particles are small enough to become airborne.

## Slide 6: Dust Exposure
Exposure to occupational dust in the workplace occurs through the breathing in of dust particles generated from work related activities, such as;
Traffic on Access & Haul Roads
Drilling & Blasting Activities
Load and Haul
Sales Trucks
Crushing & Screening Processes
Stockpiling Materials
Maintenance Activities
Weather Conditions

## Slide 7: Dust Exposure
The response of the respiratory system from exposure to occupational dust and the health effects it can have on the body, depends on the makeup and structure of the dust particles.
Without proper safety precautions, occupational dust exposure can lead to occupational dust related lung diseases, such as silicosis.

## Slide 8: Respirable Dust
Dust particles that are small enough to penetrate deep into the lungs, are called respirable.
Respirable Dust - less than 10 microns in diameter
Refer to diagram on following page which identifies respirable dust particles less than 10 microns in size as blue coloured particles, which are compared against the size of a human hair.

## Slide 9: Respirable Dust
Notes: Particles are below 30-40 microns are not visible to humans.

## Slide 10: Respirable Dust
Notes: Particles are below 30-40 microns are not visible to humans.

## Slide 11: Silica
Silica (silicon dioxide), is a naturally occurring widely abundant mineral that forms the major component of most rocks and soils.
There are non-crystalline and crystalline forms of silica.
In 1997, the International Agency for Research on Cancer (IARC) made the following evaluation that crystalline silica inhaled in the form of quartz or cristobalite from work-related sources, is carcinogenic to humans (Group 1).

## Slide 12: Crystalline Silica
The main form of crystalline silica is quartz.
Quartz Percentages:
Granite contains 25 per cent to 40 per cent quartz,
Shales average 22 per cent quartz, and
Sandstones average 67 per cent quartz.
Quartz is also the major component of sand in locations like stream beds, beaches and deserts.

## Slide 13: How Silica can Effect the Lungs
Inhaled respirable crystalline silica (RCS) dust particles can bio-accumulate in the lungs, and cause disease of the respiratory system.
These respirable particles cannot be cleared from the lungs by coughing or mucous.
Refer to Diagram on following page for a cross section of the lungs, of what areas can be effected.
i.e. secondary bronchi, bronchioles and capillary network areas.

## Slide 14: How Silica can Effect the Lungs

## Slide 15: How Silica can Effect the Lungs
The bodies defence mechanisms is to engulf the respirable crystalline silica dust particles, releasing chemicals which can lead to fibrosis and nodular lesions, and the formation of scar tissue.
The non-crystalline form of silica does not cause this kind of lung damage.

## Slide 16: Silicosis
Silicosis is the most common occupational lung disease worldwide; Silicosis resulted in 46,000 deaths globally in 2013 although down from 55,000 deaths in 1990.
Respirable crystalline silica is now known to cause chronic obstructive pulmonary disease (COPD).
Obstructive lung disease prevents a persons proper breathing and includes chronic bronchitis and emphysema.
Respirable crystalline silica remains an important risk factor for respiratory diseases and silicosis.

## Slide 17: Onset of Silicosis
There are four classifications for the onset of silicosis, these are:
Chronic,
Accelerated,
Complicated, and
Acute.

## Slide 18: Onset of Silicosis
Chronic
Chronic simple silicosis develops from long-term exposure (10 years or more) to relatively low concentrations of silica dust.
Symptoms and diagnosis develops 10–30 years after first exposure.
Chronic simple silicosis is the highest diagnosed classification within all types of silicosis.
Workers with this type of silicosis, especially early on, may not have obvious signs or symptoms of disease, but abnormalities may be detected by x-ray.
Chronic cough and shortness of breath are common findings.

## Slide 19: Onset of Silicosis
Accelerated
Accelerated silicosis develops 5–10 years after first exposure to higher concentrations of silica dust.
Symptoms and x-ray findings are similar to chronic simple silicosis, but occur earlier and tend to progress more rapidly.
Workers diagnosed with accelerated silicosis are at greater risk for complicated silicosis disease, including progressive massive fibrosis (PMF).

## Slide 20: Onset of Silicosis
Complicated
Silicosis can become “complicated” by the development of severe scaring, where the small nodules of the lungs gradually become confluent (merge together).
Progressive massive fibrosis (PMF) is associated with more severe symptoms and respiratory impairment.
Silicosis can also be complicated by other lung diseases, such as tuberculosis, fungal infections and lung cancer.
Complicated silicosis is more common with accelerated silicosis than with the chronic variety.

## Slide 21: Onset of Silicosis
Acute
Silicosis that develops a few weeks to 5 years after first exposure to high concentrations of respirable crystalline silica dust.
Symptoms of acute silicosis include more rapid onset of severe disabling shortness of breath, cough, weakness, and weight loss, often leading to death.
Silicosis can also be associated with the development of lung cancer!
Note: Several studies have also linked crystalline silica with renal disease (kidney disease).

## Slide 22: Contributing Factors
Smoking is one of the most common factors that can significantly increase the risk of contracting or exacerbate a respiratory disease condition.
Smoking and exposure to Crystalline Silica DOES NOT mean:
1 + 1 = 2 times the risk of contracting a lung disease,
The ratio is much higher:
1 + 1 = 50 times the risk of contracting a lung disease

## Slide 23: Dust Management Strategies

## Slide 24: Legislative Requirements
Aside from the Primary Duty of Care under the South Australian WHS Act 2012, there are numerous requirements under the South Australian WHS Regulations 2012, in relation to dust monitoring, dust management and health monitoring.
Please refer to the PDF file
“Dust Monitoring and Health Monitoring Legislation”
Located on our Website.

## Slide 25: Hierarchy of Control
Eliminates or Controls the Hazard or Risks
Elimination
Administrative
PPE
Isolate
Substitution
Engineering
Relies on the person working with the hazards / risks ‘doing the right thing’
remove the hazard from the workplace
use a different (safer) process, machine or chemical
as much as possible, isolate the hazard or hazardous work practice from people
install guards on machines, put in barriers around hazards
use policies, training & signs to warn workers
Notes: As with all hazards identified in the workplace, we need to use the hierarchy of controls when identifying control measures.

## Slide 26: Practical Dust Control Measures
Use strategically placed water or foam sprays to supress dust generation (can be automated)
Enclose chutes and tip points to prevent dust escaping
Use wetting agents on haul roads and stockpiles

## Slide 27: Practical Dust Control Measures
Enclosed Discharge Points Jaw Sprays

## Slide 28: Practical Dust Control Measures
Pressurised / filtered cabins and control rooms
Ensuring dust filters and ventilation systems are regularly maintained

## Slide 29: Practical Dust Control Measures
Fugitive Dust Sprays
Chemical – Spray On Water – Fan Forced

## Slide 30: Practical Dust Control Measures
Use vacuum systems rather than dry sweep
Ensure good housekeeping to prevent build up of spilt material that can become airborne
Use appropriate Personal Protective Equipment

## Slide 31: Practical Dust Control Measures
Personnel are clean shaven to ensure effective seal of respirators
Inspection and testing of cabin doors and window seals
Keep doors and windows closed
Vacuuming of cabins instead of sweeping or air blowing
Wiping instrument panels and controls with damp cloth
Reporting any leaks or damage where dust can penetrate into a sealed cabin
Replace disposable respirators regularly or when contaminated
Cleaning clothes down using a brush rather than compressed air

## Slide 32: MAQOHSC
For over 30 years the Mining and Quarrying Occupational Health and Safety Committee (MAQOHSC) has been providing health and safety assistance and support to the mining and quarrying industry of South Australia.
MAQOHSC plays a fundamental role in education of workers on occupational dust and the risks associated with exposure to respirable dust and respirable crystalline silica dust, as well as demonstrating methods to mitigate, reduce and manage the associated risks.
MAQOHSC continues to support workers and industry with professional high quality, State-wide health surveillance programs for our ever-growing industry.

## Slide 33: Further Information
MAQOHSC Work Health and Safety Specialists are available to provide further advice and assistance on all Work Health and Safety matters.
MAQOHSC Work Health and Safety Specialists are able to be contacted via our website at www.maqohsc.sa.gov.au or email maqohsc@sa.gov.au.
Work Health and Safety Legislation, Codes of Practice, fact sheets, Health and Safety Representatives (HSR) information and guides can be found at the following websites:
SafeWork SA – www.safework.sa.gov.au or call 1300 365 255
Safe Work Australia – www.safeworkaustralia.gov.au or call 1300 551 832

## Slide 34: Creative Commons
This creative commons licence allows you to copy, communicate and or adapt our work for non-commercial purposes only, as long as you attribute the work to Mining and Quarrying Occupational Health and Safety Committee and abide by all the other licence terms therein.
ISBN 978-1-925361-34-6