## Slide 1
Principal Mining Hazard :
Roads and Other Vehicles Operating Areas
April 2017

## Slide 2: The Mining and Quarrying Occupational Health and Safety Committee
Promoting Work Health and Safety in the Workplace
This workplace industry safety presentation is developed and fully funded by the Mining and Quarrying Occupational Health and Safety Committee (MAQOHSC).
ISBN 978-1-925361-46-9

## Slide 3: Disclaimer
IMPORTANT: The information in this presentation is of a general nature, and should not be relied upon as individual professional advice. If necessary, legal advice should be obtained from a legal practitioner with expertise in the field of Work Health and Safety law (SA).
Although every effort has been made to ensure that the information in this presentation is complete, current and accurate, the Mining and Quarrying Occupational Health and Safety Committee, any agent, author, contributor or the South Australian Government, does not guarantee that it is so, and the Committee accepts no responsibility for any loss, damage or personal injury that may result from the use of any material which is not complete, current and accurate.
Users should always verify historical material by making and relying upon their own separate inquiries prior to making any important decisions or taking any action on the basis of this information.

## Slide 4: Creative Commons
This creative commons licence allows you to copy, communicate and or adapt our work for non-commercial purposes only, as long as you attribute the work to Mining and Quarrying Occupational Health and Safety Committee and abide by all the other licence terms therein.

## Slide 5: What is a Principal Mining Hazard?
Regulation 612 of the Work Health and Safety Regulations 2012 (SA), defines a Principal Mining Hazard (PMH) as any:
activity, process, procedure
plant, structure, substance
situation
other circumstance relating to the carrying out of mining operations that has a reasonable potential to result in multiple deaths in a single incident or a series of recurring incidents.
Additionally, Regulation 612 identifies ‘roads and other vehicle operating areas’ as a principal mining hazard.
Notes: Regulation 34,
A duty holder, in managing risks to health and safety, must identify reasonably foreseeable hazards that could give rise to risks to health and safety.

## Slide 6: Identification and Assessment of PMHs
Regulation 627 states, a mine operator must identify all principal mining hazards at the mine and conduct a risk assessment that:
involves a comprehensive and systematic investigation and analysis of all aspects of risk with the PMH
uses appropriate investigation and analysis methods
considers the PMH individually and its interaction with other PMHs and hazards at the mine, and develops control measures.
In assessing a PMH, consideration must be given to the additional criteria outlined in Schedule 19 of the Work Health and Safety Regulations 2012 (SA).
Notes: Work Health and Safety Regulations 2012—1.1.2014
Chapter 10—Mines
Consultation and Workers' Safety Role—Part 4
675R—Mine operator must consult with workers
For the purposes of section 49(f) of the Act, the mine operator of a mine must consult with workers at the mine in relation to the following:
(b) conducting risk assessments for principal mining hazard management plans;
(d) the implementation of the workers' safety role under regulation 675Q;

## Slide 7: Consultation
Work Health and Safety legislation states, a mine operator must also consult with all personnel working at the mine / quarry and give them opportunity to contribute in the:
identification and assessment of principal mining hazards
development of principal mining hazard management plans (PMHMPs).
Consultation shall also take place with:
the health and safety committee and elected health and safety representatives (HSRs).
Note: Where a committee and HSRs are not in place, the workforce can be consulted via toolbox meetings.

## Slide 8: Schedule 19 - Additional Criteria
Under Schedule 19 of the Work Health and Safety Regulations 2012 (SA), the following matters must be considered in developing the control measures to manage the risks associated with roads and other vehicle operating areas:
Mobile plant characteristics, including stopping distances, manoeuvrability, operating speeds, driver position, driver line of sight and remote controlled mobile plant
The effect on road conditions of expected environmental conditions during operating periods, including time of day, weather, temperature and visibility
The impact of road design and characteristics, including grade, camber, surface, radius of curves and intersections
The impact of mine design, including banks and steep drops adjacent to vehicle operating areas

## Slide 9: Schedule 19 - Additional Criteria
Continued…
The volume and speed of traffic and the potential for interactions between mobile plant with different operating characteristics, including heavy and light vehicles
The potential for interactions between mobile plant and pedestrians, including consideration of park up areas and driver access
The potential for interaction between mining mobile plant and public traffic
The potential for interaction between mobile plant and fixed structures, including overhead and underground power lines, tunnel walls and roofs.

## Slide 10: Guidance on How to Comply with Schedule 19 Requirements

## Slide 11: Guidance on How to Comply with Schedule 19 Requirements
The Draft Code of Practice for Roads and other Operating Areas from Safe Work Australia looks at the following areas:
Design
Construction and Maintenance
Separation and Segregation of Vehicles and Pedestrians
Restricted Access Exclusion Zones
Vehicle Selection
Communications
Lighting
Traffic Rules
Signage
Training
Inspections and Monitoring.

## Slide 12: Design
Identifies the following areas to consider:
Terrain and geotechnical considerations
Prevailing weather and environmental conditions
Primary and secondary roads design, construction and maintenance
Road widths and gradients
Road curvature – vertical and horizontal
Sight and stopping distance
Road surface, drainage and edge protection
Intersections
Parking areas
Overhead powerlines and structures
Dumps and pads
Workshops and fixed plant areas
Runaway vehicle provisions.

## Slide 13: Construction and Maintenance
Identifies the following areas to consider:
Strength of the in-situ material used on roadways and surfaces
Wearing course or sheeting - choosing a material that will provide adequate wear and friction in the environment it is exposed to
Inspection and maintenance of its surface and drainage
Dust control - method of watering.

## Slide 14: Separation and Segregation of Vehicles and Pedestrians
Identifies the following areas to consider:
Interaction with mobile equipment and pedestrians
Interaction with light and heavy mobile equipment
Unauthorised access to operational areas including loading areas, dumps and stockpiles, workshops and plant areas and designated parking areas within these zones
Communication rules between mobile equipment / mobile equipment and mobile equipment / pedestrians
Use of engineering controls for collision avoidance.

## Slide 15: Restricted Access / Exclusion Zones
Identifies the following areas to consider:
ROM - run of mine, what material is being produced
Stockpiles and waste dumps
Drill pads
Blast pads
Haul roads
Workshops and plant areas
Stopes or unventilated areas.

## Slide 16: High Wall Drop Zones
Identifies the following areas to consider:
Haul roads located alongside high walls
Wall stability, weathing and effects of water over time
Rock falls, open joints, water damage, or overhangs
Unstable material
Restricted areas.

## Slide 17: Remotely Operated Mobile Equipment Locations
Identifies the following areas to consider:
Selection and maintenance of the remotely controlled equipment
Training and assessment of the operators
Establishment of procedures and standard work instructions
Restricted access to equipment operating areas
Communication requirements
Separation of operators and remote control equipment whilst it is operating in remote locations.

## Slide 18: Vehicle Selection
Identifies the following areas to consider:
Existing or planned road layout and conditions on site
Selected vehicles operate within their design specifications and capabilities
Drivers / operators competencies.

## Slide 19: Communications
Identifies the following areas to consider:
Communication systems
Other persons operating on roads
Communicate with each other and reporting hazards or other issues
Induction and refresher training
Radio communications policies and rules
Consistent signage
Managing changed conditions.

## Slide 20: Lighting
Identifies the following areas to consider:
Nature and type of activities being undertaken
Types of vehicles involved
Speed the vehicles will be travelling
When or where pedestrians will be encountered
Suitable lighting on vehicles such as background lighting to avoid long shadows
Use of lighting towers in operating areas
Provision of lighting in areas where pedestrians are present.

## Slide 21: Traffic Rules
Identifies the following areas to consider:
Site road layout, operating speeds and traffic flows
Right of way and signage
Vehicle operating requirements
Overtaking, parking and breakdown procedures
Radio communications
Restricted area requirements, for example, dumps, stockpiles, park bays, overhead powerlines and obstructions
Equipment separation distances and pedestrians.

## Slide 22: Signage
Identifies the following areas to consider:
Traffic sign visibility
Easy to understand
Positioned so that people have sufficient time to identify, read and react to the sign
Consistent with signage used on public roads
Maintained to ensure that they remain visible at all times and are still relevant.

## Slide 23: Training
Identifies the following areas to consider:
Induction training which includes site traffic and road rules
Specific equipment operator training
Training in road construction and maintenance.

## Slide 24: Inspections and Monitoring
Identifies the following areas to consider:
Establishing system of regular inspection and monitoring
Review of effectiveness of training provided
Pre-start inspections of equipment by operators
Regular routine equipment maintenance
Workplace inspections and monitoring of compliance by supervisors
Regular inspection and maintenance of roads, signage and traffic controls.

## Slide 25: MAQOHSC PMH Risk Assessment Tool
MAQOHSC has developed a specific risk assessment checklist tool to assist industry in managing principal mining hazards for roads and other vehicle operating areas.
The tool is based on the requirements and criteria from the Draft Code of Practice - Roads and Other Operating Areas issued by SafeWork Australia. The tool:
Covers all the elements of the Draft Code of Practice and provides a comprehensive series of questions to identify hazards and to assess risks
Contains a risk matrix and hierarchy of control
Captures the level of risk before and after controls have been implemented
Provides an area to document the findings on hazards and associated risks
Provides an area to document principal mining hazard control measures.

## Slide 26: MAQOHSC Risk Assessment Tool Cover page

## Slide 27: MAQOHSC Risk Assessment Tool Risk Matrix
RISK MATRIX |  |  | 
Exposure (E) How frequently a person(s) will be exposed to the hazard | Likelihood (L) The likelihood that harm will occur if exposed to the hazard | Consequence (C) The most likely consequence if harm does occurs | Multiply E x L x C = Risk Level
Continuously = 10 Constant exposure to the hazard during a shift | Almost Certain = 1.0 Harm is expected to occur if exposed to hazard | Catastrophic = 20 Injury resulting in a fatality | Extreme = a score more than 20 Stop work until a risk control has been implemented
Frequently = 6 Exposure to the hazard occurs several times during a shift | Likely = 0.6 Harm will probably occur if exposed to hazard | Major = 10 Injury requiring hospitalisation | High = a score between 10 & 19.9 Implement risk control within 3 days
Occasionally = 3 Exposure to the hazard occurs once a shift | Possible = 0.3 Harm could occur if exposed to hazard | Significant = 5 An injury (excluding hospitalisation or death) that requires professional medical treatment | Mod. = a score between 3 & 9.9 Implement risk control within 1 week
Infrequently = 2 Exposure to the hazard occurs once over several shifts | Unlikely = 0.1 Harm is not likely to occur if exposed to hazard | Minor = 2 Minor injury that only requires first aid | Low = a score less than 2.9 Regularly monitor the hazard
Rarely = 1 Exposure to the hazard may occur but unlikely | Rare = 0.05 Harm may occur only in exceptional circumstances if exposed to hazard | Insignificant = 1 No injuries | 

## Slide 28: MAQOHSC Risk Assessment Tool Hierarchy of Control
HIERARCHY OF CONTROL
The Hierarchy of Control must be used when determining how risks are going to be eliminated or minimised. Start at No. 1 and work down the order. Elimination – remove the hazard from the workplace Substitution – use a different (safer) process, machine or chemical Isolation – as much as possible, isolate the hazard or hazardous work practice from people Engineering – install guards on machines, put in barriers around hazards Administrative controls – use policies, training and signs to warn workers Personal protective equipment (PPE) – use gloves, glasses, hearing protection etc. PPE is always the last option used in the hierarchy of control as a means of protection!

## Slide 29: MAQOHSC Risk Assessment Tool Example
PARKING AREAS - Briefly describe the parking areas |  |  |  |  |  |  |  |  |  | 
Unattended vehicles and mobile plant rolling away from parking areas? eg, are V-drains or earthen mounds present at go-lines? |  |  |  |  |  |  |  |  |  | 
Uncontrolled movement while accessing or egressing from mobile plant and vehicles. eg, are mobile plant and vehicles fundamentally stable (on flat level ground) in V drains and vehicle shut down procedures implemented. |  |  |  |  |  |  |  |  |  | 
Uneven and downward sloped surfaces at parking areas? |  |  |  |  |  |  |  |  |  | 
The type of material used to sheet the surface of parking areas? |  |  |  |  |  |  |  |  |  | 
Muddy and slippery surface conditions of parking areas? |  |  |  |  |  |  |  |  |  | 
Layout of parking areas? eg, no standardised design, room to maneuver. |  |  |  |  |  |  |  |  |  | 
Personnel being struck by vehicle traffic in parking areas? |  |  |  |  |  |  |  |  |  | 
Personnel being struck by vehicle traffic when accessing weighbridges, offices, workshop or crushing plant areas? |  |  |  |  |  |  |  |  |  | 
Vehicle collision in or around parking areas? |  |  |  |  |  |  |  |  |  | 
Is there a possibility of injury or damage due to: | Y | N | Describe how and when injury or damage could occur | Risk Level | Describe any controls or actions to eliminate or minimise the risk of injury or damage | Revised Risk Level

## Slide 30: MAQOHSC Risk Assessment Tool Example
ROADS DESIGN, CONSTRUCTION AND MAINTENANCE - Briefly describe the primary roads design, construction and maintenance |  |  |  |  |  |  |  |  | 
Water penetrating the sub base material causing structural damage / road failure? eg, softening, sinking or collapsing. |  |  |  |  |  |  |  |  | 
Loose material on road surfaces when steering, braking or accelerating? |  |  |  |  |  |  |  |  | 
Road surface material being projected outwards by traffic? |  |  |  |  |  |  |  |  | 
Road crowns not dispersing water to the roads edges? |  |  |  |  |  |  |  |  | 
Road cross falls on corners not dispersing water to the roads edge? |  |  |  |  |  |  |  |  | 
Negative cambers on corners? |  |  |  |  |  |  |  |  | 
Corners located at the bottom of declines? |  |  |  |  |  |  |  |  | 
Is there a possibility of injury or damage due to: | Y | N | Describe how and when Injury or damage could occur | Risk Level | Describe any controls or actions to eliminate or minimise the risk of injury or damage | Revised Risk Level

## Slide 31: MAQOHSC Risk Assessment Tool Example
ROAD WIDTHS AND GRADIENTS - Briefly describe the road widths and gradients |  |  |  |  |  |  |  | 
Single lane roads? eg, accessible from both directions at the same time? |  |  |  |  |  |  |  | 
Narrow single lane road widths? eg, should be at least 1.5 times the width of the largest vehicle that travels on the road. |  |  |  |  |  |  |  | 
Narrow two-way road lane widths? eg, should be at least 3.0 times the width of the largest vehicle that travels on the road. |  |  |  |  |  |  |  | 
Operating on steep inclines and declines? eg, speed, braking, stalling Note! Gradients should be a maximum of 1 in 10 ratios. For every 10m, the gradient should rise or lower 1m. |  |  |  |  |  |  |  | 
Driving across steep inclines and declines? |  |  |  |  |  |  |  | 
Is there a possibility of injury or damage due to: | Y | N | Describe how and when Injury or damage could occur | Risk Level | Describe any controls or actions to eliminate or minimise the risk of injury or damage | Revised Risk Level

## Slide 32: MAQOHSC Risk Assessment Tool Completed Section
PARKING AREAS - Briefly describe the parking areas |  |  |  |  |  |  |  |  |  | 
 | Each Light Vehicle parking area accommodates up to 15 cars and is located at office/weighbridge and main plant, Go line located near workshop accommodates up to 10 large pieces of mobile plant (FEL and dump trucks) |  |  |  |  |  |  |  |  | 
Unattended vehicles and mobile plant rolling away from parking areas? eg, are V-drains or earthen mounds present at go-lines? |  | X |  | Light vehicle parking areas at office weighbridge located on uneven ground – vehicle rollaway Go line areas have no earthen mound – vehicle rollaway | H | Level all parking areas Provide earthen mounds around car parking areas and go line areas for 3rd party protection |  |  | L | 
Uncontrolled movement while accessing or egressing from mobile plant and vehicles. eg, are mobile plant and vehicles fundamentally stable (on flat level ground) in V drains and vehicle shut down procedures implemented. |  | X |  | Go line area has no V drains – vehicle not fundamentally stable when parked No procedure for operation and shut down of mobile plant Workers not trained in mobile plant operations | H | Provide V drains at go line to ensure all mobile plant are fundamentally stable when parked and personnel accessing and egressing cabins Conduct a risk assessment on the mobile plant and its operations and generate procedures for operations Train workers in mobile plant operation procedures |  |  | M | 
Uneven and downward sloped surfaces at parking areas? |  | X |  | Light vehicle and go line parking area have pot hole which could cause trip slip hazard | H | Fill in all pot holes and conduct regular inspections to ensure surfaces are maintained |  |  | L | 
The type of material used to sheet the surface of parking areas? |  | X |  | Surface of parking area is sheeted with a clay material which could cause vehicle loss of control when braking or pedestrian slipping in wet weather conditions | H | Sheet surface with 5mm aggregate or fine rubble |  |  | L | 
Muddy and slippery surface conditions of parking areas? |  | X |  | Go line area has pooled water around vehicle parking zones creating muddy / slippery conditions for operators – potential slip hazard | M | Fill sunken areas with suitable material to prevent water pooling and conduct regular inspections to ensure surfaces are maintained |  |  | L | 
Layout of parking areas? eg, no standardised design, room to manouver |  | X |  | No delineated / marked areas to inform light vehicle drivers how to appropriately park | M | Delineate / mark surfaces or sign where and how light vehicles are required to park |  |  | L | 
Personnel being struck by vehicle traffic in parking areas? |  |  | X | Segregated and delineated walkways are in place to direct pedestrians in and out of parking areas |  |  |  |  |  | 
Personnel being struck by vehicle traffic when accessing weighbridges, offices, workshop or crushing plant areas? |  |  | X | Segregated and delineated walkways are in place to direct pedestrians to and from office / weighbridge and workshop |  |  |  |  |  | 
Vehicle collision in or around parking areas? |  | X |  | No speed limit designated for parking areas No one-way entry and exit points installed | H | Identify and install suitable speed limit for parking areas in relation to size of vehicles operating within them Establish one-way entry and exit points to parking areas |  |  | M | 
Is there a possibility of injury or damage due to: | Y | N | Describe how and when Injury or damage could occur | Risk Level | Describe any controls or actions to eliminate or minimise the risk of injury or damage | Revised Risk Level

## Slide 33: MAQOHSC Risk Assessment Tool Corrective action plan
Corrective action plan |  |  |  |  | 
Safe Operating Procedures (SOP): |  |  |  |  | 
Recommendations on Methods for Ensuring Safe Work |  |  |  |  | 
Where a Safe Operating Procedure is developed, this Risk Assessment needs to be referenced within the document. |  |  |  |  | 
Action Plan |  |  |  |  | 
Action No | Action required | Risk Level | Responsibility | Completion Date | Review Date
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
16 |  |  |  |  | 
17 |  |  |  |  | 
18 |  |  |  |  | 
19 |  |  |  |  | 
20 |  |  |  |  | 
21 |  |  |  |  | 
22 |  |  |  |  | 
23 |  |  |  |  | 
24 |  |  |  |  | 
25 |  |  |  |  | 
26 |  |  |  |  | 
27 |  |  |  |  | 
28 |  |  |  |  | 
29 |  |  |  |  | 
30 |  |  |  |  | 
31 |  |  |  |  | 
32 |  |  |  |  | 
33 |  |  |  |  | 
34 |  |  |  |  | 

## Slide 34: Preparation of Principal Mining Hazard Management Plans
A Principal Mining Hazard Management Plan (PMHMP) must:
Provide for the management of all aspects of risk control in relation to the relevant principal mining hazard
Be set out and expressed in a way that is readily accessible and understandable to all persons who use it.

## Slide 35: Principal Mining Hazard Management Plan
ID | PMHMP - 02
Title | Surface Mobile Equipment
Management Strategy | Due to the nature of operations at XYZ, surface mobile equipment (SME) is utilised throughout the site. SME operations are managed as per relevant SME operational procedures.
Relationship to other hazards | Relationship to other PMHs include: Fatigue Light Vehicle operation Falls from height Stored Energy Additional hazard relationships and control measures shall be managed on a task-by-task basis, via the job safety analysis process.
Identification methods | PMHs are identified by the following methods: Hazard reports Risk registers Investigations Audits Professional consultation Industry standards, knowledge and practices HSR meetings, toolbox talks and PSIs
Communication, Consultation and Training | This Principal Mining Hazard Management Plan (PMHMP) has been developed and reviewed in consultation with workers on site. Identified PMHs shall be communicated to workers via inductions and reiterated through sign boards, PSI meetings, intranet and other formal communication channels used on site. A hard copy of this document shall be kept on site and made accessible to workers and visitors.

## Slide 36: Review of Principal Mining Hazard Management Plans
The mine operator of a mine / quarry must ensure that any Management Plan developed for a Principal Mining Hazard:
Is reviewed on a regular basis
As necessary, revised if a risk control measure specified in the plan is revised under Regulation 38 or Regulation 618 of the Work Health and Safety Regulations 2012 (SA).
Notes: 38—Review of control measures
A duty holder must review and, as necessary, revise control measures implemented under these regulations so as to maintain, so far as is reasonably practicable, a work environment that is without risks to health or safety.
Without limiting subregulation (1), the duty holder must review and, as necessary, revise a control measure in the following circumstances:
  the control measure does not control the risk it was implemented to control so far as is reasonably practicable;
Examples—
    The results of monitoring show that the control measure does not control the risk.
    A notifiable incident occurs because of the risk.
  before a change at the workplace that is likely to give rise to a new or different risk to health or safety that the measure may not effectively control;
  a new relevant hazard or risk is identified;
  the results of consultation by the duty holder under the Act or these regulations indicate that a review is necessary;
  a health and safety representative requests a review under subregulation (4).
Without limiting subregulation (2)(b), a change at the workplace includes—
  a change to the workplace itself or any aspect of the work environment; or
  a change to a system of work, a process or a procedure.
A health and safety representative for workers at a workplace may request a review of a control measure if the representative reasonably believes that—
  a circumstance referred to in subregulation (2)(a), (b), (c) or (d) affects or may affect the health and safety of a member of the work group represented by the health and safety representative; and
  the duty holder has not adequately reviewed the control measure in response to the circumstance.
618—Review of control measures
A person conducting a business or undertaking at a mine must review and as necessary revise control measures implemented under regulation 617 in the following circumstances:
  an audit of the effectiveness of the safety management system for the mine indicates a deficiency in a control measure;
  a worker is moved from a hazard or assigned to different work in response to a recommendation contained in a health monitoring report provided under Part 3;
  an incident referred to in regulation 675V occurs.
Notes—
    WHS Act—sections 19, 20 and 21, as applicable (see regulation 9).
    This requirement is in addition to the requirement under regulation 38 (see regulation 33).
    This regulation applies to a mine operator (see regulation 613(3)).
The mine operator of a mine must ensure that a control measure that is the subject of a request by a health and safety representative under regulation 38(4) is reviewed and as necessary revised, whether the request is made directly to the mine operator or notified to the mine operator under subregulation (3) by another person conducting a business or undertaking at the mine.
Notes—
    WHS Act—sections 19, 20 and 21, as applicable (see regulation 9).
    This requirement is in addition to the requirement under regulation 38 (see regulation 33).
A person conducting a business or undertaking at the mine who is not the mine operator of the mine must immediately notify the mine operator of a request made to the person under regulation 38(4).
Maximum penalty:
(a) in the case of an individual—$6 000;
(b) in the case of a body corporate—$30 000.
A health and safety representative for workers at the mine may request a review of a control measure under regulation 38(4) as if the circumstances referred to in subregulation (1) were included in regulation 38(4)(a).

## Slide 37: Further Assistance
MAQOHSC Work Health and Safety Specialists are available to provide further on-site support and assistance on all Work Health and Safety matters.
MAQOHSC Work Health and Safety Specialists can be contacted via our online support request form available on our website at www.maqohsc.sa.gov.au or email maqohsc@sa.gov.au.
Work Health and Safety Legislation, Codes of Practice, fact sheets, Health and Safety Representatives (HSR) information and guides can be found at the following websites:
SafeWork SA – www.safework.sa.gov.au or call 1300 365 255
Safe Work Australia – www.safeworkaustralia.gov.au or call 1300 551 832