| Inspectors Name: Assistant 1 Assistant 2 |
| --- |
| Crushing Plants: |  |  |
|  |  | Site |  | Date |  | Time |  |  |
| Instructions for personnel completing this Inspection; It is recommended this inspection be completed monthly. It is recommended a minimum of 2 persons conduct the inspection, one should be a health and safety representative of the work group (if present at the worksite) or a person qualified or experienced in Work Health and Safety and the other, a member of the workgroup, Complete the checklist below by ticking / marking the applicable score (Y, N, N/A) for each item. Complete details of non-conformances identified in the space provided. Assign a risk score for each non-conformance using the matrix below. Complete details including: Name, Date and signature in the space provided. Return the completed form to the (insert role or dept., e.g. Area Manager, Safety Dept., etc.) for corrective actions to be assigned. |

| RISK MATRIX | HIERARCHY OF CONTROL |
| --- | --- |
| Likelihood | Consequences | The Hierarchy of Control must be used when determining how risks are going to be Eliminated or Minimised. Start at No. 1 and work down the order. Elimination – remove the hazard from the workplace Substitution – use a different (safer) process, machine or chemical Isolation - as much as possible, isolate the hazard or hazardous work practice from people. Engineering – install guards on machines, put in barriers around hazards Administrative controls – use policies, training and signs to warn workers Personal protective equipment (PPE) – use gloves, glasses, hearing protection etc. Personal protective equipment is always the last option used in the hierarchy of control as a means of protection! |
|  | 1 Insignificant | 2 Minor | 3 Moderate | 4 Major | 5 Catastrophic |  |
| A - Almost Certain | M | H | E | E | E |  |
| B - Likely | M | H | H | E | E |  |
| C - Possible | L | M | H | H | E |  |
| D - Unlikely | L | L | M | H | H |  |
| E - Rare | L | L | M | H | H |  |

| Risk Matrix Legends |
| --- |
| Rating | Safety | Health | Environment |
| 1 Minor | Single minor injury to one person. First aid or no treatment required. No lost time. | Reversible health effects of minor concern only requiring minor first aid treatment. | Issues of non-continuous nature with promptly reversible impact or consequence (e.g. within shift). Low-level incident, site contained. |
| 2 Moderate | Medically treated injury. Reversible injury. Does not lead to restricted duties. | Reversible health effects of concern that results in medical treatment but does not lead to restricted duties. | Issues of a non-continuous nature and minor impact and consequence. Low-level incident, site contained. Short term reversible (e.g. within days). |
| 3 Serious | Reversible injury or moderate irreversible impairment. Less than 10 days lost time. | Severe but reversible health effects. Results in a lost time illness of less than 10 days. | Issues of a continuous nature - limited impact and consequence Incident resulting in some site contamination. Medium term recovery impact. |
| 4 Major | Severe irreversible damage to one or more persons. Lost Time Injury greater than 10 days. | Severe and irreversible health effects or disabling illness. | Compliance issue with large fine, media attention. Serious harm not immediately recovered. Significant site contamination or off-site impact. Long term recovery. |
| 5 Catastrophic | Fatality. Permanent disabling injuries. | Life threatening or permanently disabling illness. | Issues of a continuous nature with major long-term impact and potentially serious consequences. |
| Rating | Descriptor | Description | Suggested Frequency |
| A | Almost certain | The event is expected to occur | Recurring event during the lifetime of a project/operation, e.g. More than once per month |
| B | Likely | The event will probably occur | Event that may occur frequently during the lifetime of a project/operation, e.g. At least once per year |
| C | Possible | The event should occur | Event that may occur during the lifetime of a project/operation e.g. Once in 3 years |
| D | Unlikely | The event could occur | Event that is unlikely to occur during the lifetime of a project/operation e.g. Once in 10 years |
| E | Rare | The event may occur only in exceptional circumstances | Event that is very unlikely to occur during the lifetime of a project/operation, e.g. Once in 15 years |
| Rating | Definition | Level of Involvement |
| Extreme | Cease work - No works shall be conducted until controls are implemented to reduce the risk level. Immediate formal risk assessment required. | The most senior person on site (Chief Executive Officer, Managing Director, General Manager) must review and approve risk control measures before allowing work to recommence |
| High | Corrective action required. Normally permits required to perform work. Safe Work Procedure or Job Hazard Analysis is mandatory. | Mine Operator and or Quarry Manager review required |
| Moderate | Corrective action required. Job Hazard Analysis or Safe Work Procedure required. | Supervisor / Superintendent review required |
| Low | Corrective action where practical. Take 5 risk assessment required. | Supervisor to manage by routine procedures at operational level |

| GENERAL |
| --- |
| Do the operators have a Certificate of Competency or VOC for the mobile plant and crushing / screening plants they are operating? (check training records) |  |  |  |  |  |  |
| Have the operators completed a pre-start checklist for the crushing / screening plants? |  |  |  |  |  |  |
| Have the operators completed a pre-start checklist for the mobile plant they are operating? |  |  |  |  |  |  |
| Have the operators completed a Take Time Take Charge (or similar)? |  |  |  |  |  |  |
| Is there a functional “Two Way” communications system? |  |  |  |  |  |  |
| Is the overall appearance of the area neat and tidy? |  |  |  |  |  |  |
| Does all wiring / hosing appear to be in good order and neatly stored out of the way? |  |  |  |  |  |  |
| Do dust emissions appear to be under control? |  |  |  |  |  |  |
| Is there suitable and adequate lighting for pre-dawn and after sunset operations? |  |  |  |  |  |  |
| Is there suitable access to the mobile plant that is loading the primary hopper? |  |  |  |  |  |  |
| If using an Excavator, ensure that there is a “trough” between the “High Wall” and the Excavator? |  |  |  |  |  |  |

| If using a Loader, is the loading ramp even and of sufficient width to operate safely? Are side bunds in place? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| If using a Loader, does the loading ramp have side bunds / edge protection in place? |  |  |  |  |  |  |
| PRIMARY PAD AREA |
| Is the Pad area level with at least 1m clearway all around? |  |  |  |  |  |  |
| Is the warning signage clean and legible? |  |  |  |  |  |  |
| Is the area free from trip hazards e.g. rocks on access / walkways of the pad area? e.g. spillage |  |  |  |  |  |  |
| Is there unobstructed access for the service vehicle? |  |  |  |  |  |  |
| PRIMARY TRACK AND FRAME |
| Are the grousers / track plates in good condition (loose, missing, bent, worn etc.)? |  |  |  |  |  |  |
| Are the idlers, pulleys in good condition? |  |  |  |  |  |  |
| Are the tracks “tight”? |  |  |  |  |  |  |
| Is the area free from any major structural damage (bolts missing, broken welds, bent sections etc.)? |  |  |  |  |  |  |
| PRIMARY JAW AREA AND ACCESS |
| Are all fire extinguishers correctly tagged, sign posted and charged? |  |  |  |  |  |  |

| Are warning signs present? e.g. emergency stop, restricted access |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Is the warning signage clean and legible? |  |  |  |  |  |  |
| Are Emergency Stop Buttons easily accessible, identifiable and functioning properly? |  |  |  |  |  |  |
| Are the Chains / Gates preventing access secured / closed? |  |  |  |  |  |  |
| Are the steps and handrails in good condition and allow three points of contact? |  |  |  |  |  |  |
| Are the Stairways / Walkways free from trip hazards and obstructions? |  |  |  |  |  |  |
| Are the control panels clean and in good order (doors closing / lockable etc.) |  |  |  |  |  |  |
| Are all warning lights working correctly on the control panel? (test button) |  |  |  |  |  |  |
| Are all lights working correctly on the rig? |  |  |  |  |  |  |
| Is the rock breaker (where fitted) functioning properly? (observe active test) |  |  |  |  |  |  |
| Is the area free from any significant leaks around the rock breaker and controls? |  |  |  |  |  |  |
| Is guarding in place to prevent access to dangerous moving parts (access to jaw area etc.) |  |  |  |  |  |  |
| Is the Guarding around the rock breaker in good order? |  |  |  |  |  |  |

| Is the Guarding around the Jaw in good order? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Do the rams appear to be in good condition and free from pitting and scoring? |  |  |  |  |  |  |
| PRIMARY DISCHARGE CONVEYOR |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |

| SIDE SCALPS CONVEYOR |
| --- |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| SCREENING UNIT PAD AREA |
| Is the Pad area level with at least 1m clearway all around? |  |  |  |  |  |  |
| Is the warning signage clean and legible? |  |  |  |  |  |  |
| Is the area free from any trip hazards e.g. rocks on access / walkways of the pad area? e.g. spillage |  |  |  |  |  |  |
| Is there unobstructed access for the service vehicle? |  |  |  |  |  |  |
| SCREENING UNIT TRACK AND FRAME |
| Are the grousers / track plates in good condition (loose, missing, bent, worn etc.)? |  |  |  |  |  |  |
| Are the idlers, pulleys in good condition? |  |  |  |  |  |  |
| Are the Tracks “Tight”? |  |  |  |  |  |  |
| Is the area free from any major structural damage (bolts missing, broken welds, bent sections etc.)? |  |  |  |  |  |  |
| Are the stabiliser legs down and locking pins inserted? |  |  |  |  |  |  |
| SCREENING AREA AND ACCESS |
| Are all fire extinguishers correctly tagged, sign posted and charged? |  |  |  |  |  |  |
| Are warning signs present? e.g. emergency stop, restricted access |  |  |  |  |  |  |
| Is the warning signage clean and legible? |  |  |  |  |  |  |
| Are Emergency Stop Buttons easily accessible and identifiable and functioning properly? |  |  |  |  |  |  |
| Are the Chains / Gates preventing access secured / closed? |  |  |  |  |  |  |

| Are the steps and handrails in good condition and allow three point contact? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Are the Stairways / Walkways free from trip hazards and obstructions? |  |  |  |  |  |  |
| Are the control panels clean and in good order (doors closing / lockable etc.) |  |  |  |  |  |  |
| Are all warning lights working correctly on the control panel? (test button) |  |  |  |  |  |  |
| Are all lights working correctly on the unit? |  |  |  |  |  |  |
| Is the Guarding around the screen mechanisms in good order? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| Are the springs on the screen deck in good condition and free from broken sections? |  |  |  |  |  |  |
| Is the area free from any “loose material” build up on any of the framework / ledges? |  |  |  |  |  |  |
| FEED CONVEYOR (UNDER HOPPER) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |

| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| LIFT CONVEYOR (DISCHARGE ONTO SCREEN) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| DISCHARGE CONVEYOR (TO STACKER) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| STACKER CONVEYOR |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Do skirt rubbers appear to be in good condition? (look for spillage, dust) |  |  |  |  |  |  |
| SIDE CONVEYOR (TO SECONDARY CRUSHER) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |

| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| SIDE CONVEYOR (NON - FUNCTIONAL SIDE) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is the Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| SIDE CONVEYOR (NON - FUNCTIONAL SIDE) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| SECONDARY PAD AREA |
| Is the Pad area level with at least 1m clearway all around? |  |  |  |  |  |  |
| Is the warning signage clean and legible? |  |  |  |  |  |  |
| Is the area free from trip hazards e.g. rocks on access / walkways of the pad area? e.g. spillage |  |  |  |  |  |  |

| Is there unobstructed access for the service vehicle? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| SECONDARY TRACK AND FRAME |
| Are the grousers / track plates in good condition (loose, missing, bent, worn etc.)? |  |  |  |  |  |  |
| Are the idlers, pulleys in good condition? |  |  |  |  |  |  |
| Are the tracks “tight”? |  |  |  |  |  |  |
| Is the area free from any major structural damage (bolts missing, broken welds, bent sections etc.)? |  |  |  |  |  |  |
| SECONDARY CONE AREA AND ACCESS |
| Are all fire extinguishers correctly tagged, sign posted and charged? |  |  |  |  |  |  |
| Are warning signs present? e.g. emergency stop, restricted access |  |  |  |  |  |  |
| Is the warning signage clean and legible? |  |  |  |  |  |  |
| Are Emergency Stop buttons Easily accessible and identifiable and functioning properly? |  |  |  |  |  |  |
| Are the Chains / Gates preventing access secured / closed? |  |  |  |  |  |  |
| Are the steps and handrails in good condition and allow three point contact? |  |  |  |  |  |  |
| Are the Stairways / Walkways free from trip hazards and obstructions? |  |  |  |  |  |  |

| Are the control panels clean and in good order (doors closing etc.) |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Are all warning lights working correctly on the control panel? (test button) |  |  |  |  |  |  |
| Are all lights working correctly on the rig? |  |  |  |  |  |  |
| Is the Cone appropriately guarded? |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| Is the area free from any “loose material” build up on any of the framework, ledges? |  |  |  |  |  |  |
| Is the condition of the mantle in good condition? (no cracks, excessive wear etc.) |  |  |  |  |  |  |
| LIFT CONVEYOR (TO THE CONE) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Do skirt rubbers appear to be in good condition? (look for spillage, dust) |  |  |  |  |  |  |
| DISCHARGE CONVEYOR (UNDER THE CONE) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? |  |  |  |  |  |  |
| Are conveyor inspection covers in place? |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Do skirt rubbers appear to be in good condition? (look for spillage, dust) |  |  |  |  |  |  |

| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| STACKER CONVEYOR (TO THE HOPPER) |
| Is the conveyor belt in good condition? (free of cuts, holes, wear etc.) |  |  |  |  |  |  |
| Are Emergency Stop lanyards clearly marked and easily accessible? |  |  |  |  |  |  |
| Do Lanyards have a “Direct” line of pull? (straight) |  |  |  |  |  |  |
| Is Tail Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Is Head Drum inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Trough Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Are Return Idlers inaccessible or securely guarded? |  |  |  |  |  |  |
| Is the area free from any spillage or excessive dust emissions from the conveyor? |  |  |  |  |  |  |
| Do skirt rubbers appear to be in good condition? (look for spillage, dust) |  |  |  |  |  |  |
| Are the grease points easily accessible and appear to be functional? |  |  |  |  |  |  |
| Are the tyres in good condition? |  |  |  |  |  |  |
| Do the axles and framework appear to be in good condition? |  |  |  |  |  |  |
| Are the wheels chocked? |  |  |  |  |  |  |
| Do the height adjusting arms have locking pins and clips? |  |  |  |  |  |  |
| SIGN OFF |
| Person conducting Inspection |  | Signature |  | Date of Report |  |

| CORRECTIVE ACTION PLAN |
| --- |
| Action No | Action required | Responsibility | Completion Date | Review Date |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |
| 12 |  |  |  |  |
| 13 |  |  |  |  |
| 14 |  |  |  |  |
| 15 |  |  |  |  |
| 16 |  |  |  |  |
| 17 |  |  |  |  |
| 18 |  |  |  |  |
| 19 |  |  |  |  |
| 20 |  |  |  |  |