PREPARATION:

Before undertaking a risk assessment:

- Select personnel to be a part of the risk assessment team and a leader of the team should be appointed.

- The leader of the team should be a competent person (have the skills, knowledge and experience) to undertake the risk management process and have a good understanding of the work processes to be assessed.

- All persons involved in the risk assessment should have an understanding of the work processes to be assessed.

- The team should consist of management / supervision, a health and safety representative (where elected) and a worker directly related to the work.

- The risk assessment team should consult with the worker(s) who undertake the work, or who will be directly affected by the work.

The leader of the risk assessment team should:

- Consult with those involved and agree on a date and time to undertake the risk assessment.

- Ensure the team has the appropriate resources available for the assessment, i.e. note pads, pens, tape measure, level and noise meter (where necessary).

- Ensure the plant or chemical substances associated with the work processes are available during the risk assessment.

- Have copies of plant and equipment operating manuals, operating procedures and maintenance manuals, along with any safety data sheets (SDS) for substances to be used or produced during the work processes.

The risk assessment team should:

- Review the pre purchase risk assessment for any new plant or hazardous chemicals (where completed) to identify any pre-existing hazards that will need to be assessed.

- Review the risk assessment checklist to ensure they fully understand how it is to be used.

- Risk assessment the work process under normal operating conditions (or simulate where not practical).

CONDUCTING THE RISK ASSESSMENT:

The risk assessment team, in consultation with the worker(s) who undertake the work, or who will be directly affected by the work, should conduct the risk assessment in the following manner:

- The risk assessment team leader to complete the details on the second page of the risk assessment checklist.

- The team should assess each key step of the work process including the preparation, undertaking the work and the cleanup processes etc.

- Complete each part of the risk assessment checklist by answering the questions in each category of the checklist in the following manner:

  - Identify any Hazard and tick YES where there is a possibility of injury or damage or NO where there is not;

  - Where YES has been ticked, describe the Hazard (how and when the injury or damage could occur);

  - Assess the risk of injury or damage from the Hazard using the risk matrix:

    - Assess the likelihood of injury or damage as a result of coming into contact with the hazard and select a level indicator; and

    - Assess the most likely consequences as a result of injury or damage occurring and select a level indicator.

- Follow the likelihood column across and the consequences column down on the risk matrix to the point where they both meet to obtain the risk level (rating) for each Hazard.

- Document the risk level in the risk rating column and identify and document the appropriate risk controls and actions using the hierarchy of control for each hazard identified.

- Reassess the risk level after risk controls and actions have been implemented.

COMPLETING ACTION PLAN

The team in consultation with relevant workgroup should:

- Record each risk control and action in the corrective action plan located at the end of the document.

- Assign time frame / date for completion, person(s) responsible for corrective action completion, and review with regular meetings for close out of outstanding actions.

- Verification of the completed actions needs to be completed by management and documented.

MONITORING AND REVIEWING RISK CONTROLS

The risk assessment team in consultation with relevant workgroup:

- Should monitor and review each risk control and action to ensure controls are effective and no other hazards have been created and introduced into the work.

| REASONS FOR RISK ASSESSMENT |
| --- |
| Company: |  |  |
|  |  | Site Location |  |  |
| Is the risk assessment due to new or proposed changes to plant and equipment, a work process, hazardous chemicals or the environment? | YES |  | NO |  |  |
| If Yes, please tick the corresponding box: | Plant and Equipment? |  | Work Process? |  | Hazardous Chemicals? |  | Environment? |  |  |
| Describe the change: |  |  |
| If No is the risk assessment required due to a hazard that has not been previously risk assessed? (Please tick) | YES |  | NO |  |  |
| If Yes, was the hazard identified as a result of Hazard Report? (Please tick) | YES |  | NO |  |  |
| If No, was the hazard identified as a result of Incident Report? (Please tick) |  | YES |  | NO |  |  |
| If none of the above describe the reasons for the risk assessment review e.g. safety management system / document review |  |  |
| Additional Details or Comments: |

|  | RISK ASSESSMENT - DESCRIPTION | Risk Assessment Completed By |
| --- | --- | --- |
| Description of Activities: |  |  | Name: |  |  |
|  |  |  | Title: |  |  |
| Location of Activities: |  |  |  |  |  |
| Personnel Exposed: |  |  | Worker(s) Consulted: |  |  |
| Additional Comments: |  |  | Date Conducted: |  |  |

| RISK MATRIX | HIERARCHY OF CONTROL |
| --- | --- |
| Likelihood | Consequences | The Hierarchy of Control must be used when determining how risks are going to be Eliminated or Minimised. Start at No. 1 and work down the order. Elimination – remove the hazard from the workplace Substitution – use a different (safer) process, machine or chemical Isolation - as much as possible, isolate the hazard or hazardous work practice from people Engineering – install guards on machines, put in barriers around hazards Administrative controls – use policies, training and signs to warn workers Personal protective equipment (PPE) – use gloves, glasses, hearing protection etc. Personal protective equipment is always the last option used in the hierarchy of control as a means of protection! |
|  | 1 Insignificant | 2 Minor | 3 Moderate | 4 Major | 5 Catastrophic |  |
| A - Almost Certain | M | H | E | E | E |  |
| B - Likely | M | H | H | E | E |  |
| C - Possible | L | M | H | H | E |  |
| D - Unlikely | L | L | M | H | H |  |
| E - Rare | L | L | M | H | H |  |

| Risk Matrix Legends |
| --- |
| Rating | Safety | Health | Environment |
| 1 Minor | Single minor injury to one person. First aid or no treatment required. No lost time. | Reversible health effects of minor concern only requiring minor first aid treatment. | Issues of non-continuous nature with promptly reversible impact or consequence (e.g. within shift). Low-level incident, site contained. |
| 2 Moderate | Medically treated injury. Reversible injury. Does not lead to restricted duties. | Reversible health effects of concern that results in medical treatment but does not lead to restricted duties. | Issues of a non-continuous nature and minor impact and consequence. Low-level incident, site contained. Short term reversible (e.g. within days). |
| 3 Serious | Reversible injury or moderate irreversible impairment. Less than 10 days lost time. | Severe but reversible health effects. Results in a lost time illness of less than 10 days. | Issues of a continuous nature - limited impact and consequence Incident resulting in some site contamination. Medium term recovery impact. |
| 4 Major | Severe irreversible damage to one or more persons. Lost Time Injury greater than 10 days. | Severe and irreversible health effects or disabling illness. | Compliance issue with large fine, media attention. Serious harm not immediately recovered. Significant site contamination or off-site impact. Long term recovery. |
| 5 Catastrophic | Fatality. Permanent disabling injuries. | Life threatening or permanently disabling illness. | Issues of a continuous nature with major long-term impact and potentially serious consequences. |
| Rating | Descriptor | Description | Suggested Frequency |
| A | Almost certain | The event is expected to occur | Recurring event during the lifetime of a project/operation e.g. More than once per month |
| B | Likely | The event will probably occur | Event that may occur frequently during the lifetime of a project/operation e.g. At least once per year |
| C | Possible | The event should occur | Event that may occur during the lifetime of a project/operation e.g. Once in 3 years |
| D | Unlikely | The event could occur | Event that is unlikely to occur during the lifetime of a project/operation e.g. Once in 10 years |
| E | Rare | The event may occur only in exceptional circumstances | Event that is very unlikely to occur during the lifetime of a project/operation e.g. Once in 15 years |
| Rating | Definition | Level of Involvement |
| Extreme | Cease work - No works shall be conducted until controls are implemented to reduce the risk level. Immediate formal risk assessment required. | The most senior person on site (Chief Executive Officer, Managing Director, General Manager) must review and approve risk control measures before allowing work to recommence |
| High | Corrective action required. Normally permits required to perform work. Safe Work Procedure or Job Hazard Analysis is mandatory. | Mine Operator and or Quarry Manager review required |
| Moderate | Corrective action required. Job Hazard Analysis or Safe Work Procedure required. | Supervisor / Superintendent review required |
| Low | Corrective action where practical. Take 5 risk assessment required. | Supervisor to manage by routine procedures at operational level |

| WORKING CONDITIONS – summarise: (isolated or remote), start and finish times, number of days per week, hours per day, overtime requirements |
| --- |
| Working alone / isolated or remotely from other workers? Note: refer to the Code of Practice - Managing the Work Environment and Facilities. |  |  |  |  |  |  |
| Not being able to contact others for assistance in the event of an emergency? |  |  |  |  |  |  |
| Bullying, harassment, violence or threatening behaviour between workers? |  |  |  |  |  |  |
| Fatigue from working constant extended shifts (overtime) or double shifts Note: refer to the SafeWork Australia - Guide for Managing the Risk of Fatigue at Work. |  |  |  |  |  |  |
| Fatigue from performing repetitious, monotonous work or concentrating for extended periods of time? |  |  |  |  |  |  |
| Fatigue from work requiring continuous physical effort? |  |  |  |  |  |  |
| Being effected by dust, odours or fumes? |  |  |  |  |  |  |
| Poor visibility from reflective objects, bright lights, sun glare, excessive dust or reduced lighting? |  |  |  |  |  |  |
| Exposure to UV radiation from the sun? |  |  |  |  |  |  |
| Excessive temperatures when working indoors or outdoors? (Hot / Cold) |  |  |  |  |  |  |
| Working in a confined space? Note: refer to the Code of Practice – Confined Space. |  |  |  |  |  |  |
| Falling from one level to another while working at height? Note: refer to the Code of Practice - Managing the Risks of Falls at Workplaces. |  |  |  |  |  |  |
| Slips, trips or falls at ground level or below? Note: refer to the Code of Practice - Managing the Risks of Falls at Workplaces. |  |  |  |  |  |  |

| Working on a fragile roof? Perspex / fibrous cement / asbestos sheeting. Note: refer to the Code of Practice - Managing the Risks of Falls at Workplaces. |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Being struck by moving mobile plant or vehicles? Note: refer to the MAQOHSC Traffic Management Guide. |  |  |  |  |  |  |
| Being engulfed by a free flowing solid or liquid? |  |  |  |  |  |  |
| Being struck by a falling object that is being carried, transported or lifted? |  |  |  |  |  |  |
| Suffocation or being crushed from falling or collapsing materials or a structure? |  |  |  |  |  |  |
| Head, body or limb contact on plant or equipment due to restricted movement in the work area? |  |  |  |  |  |  |
| Electrocution from contact with powerlines, electrical cables or exposed wiring? |  |  |  |  |  |  |
| Being exposed to or working with asbestos related materials during their work? Note: refer to the Code of Practice - How to manage Asbestos in the Workplace. |  |  |  |  |  |  |
| Being stung, bitten or struck by an insect or animal? |  |  |  |  |  |  |
| Background noise above 85db? Note: refer to the Code of Practice - Managing Noise and Preventing Hearing Loss at Work. |  |  |  |  |  |  |

| HAZARDOUS MANUAL TASKS – Summarise: tasks and associated equipment used |
| --- |
| Note! The following section is from the Code of Practice for Hazardous Manual Tasks - Refer to the Code for guidance on control measures Definitions: Repetitive means: the movement or force is performed more than twice a minute, Sustained means: the posture or force is held for more than 30 seconds at a time |
| Step 1: Does the task involve repetitive or sustained movements, postures or forces? If you tick yes then the task is a risk and must be controlled |
| Body Part: Neck or Head |
| Bending more than 20 degrees | forward |  |  |  |  |  |  |
|  | sideways |  |  |  |  |  |  |

|  | twisting |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bending more than 5 degrees | backward |  |  |  |  |  |  |
| Body Part: Back |
| Bending more than 20 degrees | forward |  |  |  |  |  |  |
|  | sideways |  |  |  |  |  |  |
|  | twisting |  |  |  |  |  |  |
| Bending more than 5 degrees | backward |  |  |  |  |  |  |
| Body Part: Arms / Hand |
| Working with one or both hands above shoulder height |  |  |  |  |  |  |
| Reaching forwards or sideways more than 30cm from the body |  |  |  |  |  |  |
| Reaching behind the body |  |  |  |  |  |  |
| Excessive bending of the wrist |  |  |  |  |  |  |
| Twisting, turning grabbing, picking or wringing actions with the fingers, hands or arms |  |  |  |  |  |  |
| Body Part: Legs |
| Squatting, kneeling, crawling, lying or jumping |  |  |  |  |  |  |

| Standing with most of the body’s weight on one leg |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Very Fast Movements |
| Lifting or lowering |  |  |  |  |  |  |
| Carrying with one hand or one side of the body |  |  |  |  |  |  |
| Exerting force with one hand or one side of the body |  |  |  |  |  |  |
| Pushing, pulling or dragging |  |  |  |  |  |  |
| Very fast actions |  |  |  |  |  |  |
| Working with the fingers close together or wide apart |  |  |  |  |  |  |
| Applying uneven, fast or jerky forces |  |  |  |  |  |  |
| Holding, supporting or restraining anything |  |  |  |  |  |  |
| Step 2: Does the task in step 1 involve long duration? If you tick yes then the task is a risk and must be controlled |
| More than 2 hours over a whole shift |  |  |  |  |  |  |
| Continually for more than 30 minutes at a time |  |  |  |  |  |  |
| Step 3: Does the task involve high or sudden force? If you tick yes then the task is a risk and must be controlled |
| Lifting, lowering or carrying heavy loads |  |  |  |  |  |  |
| Hitting, throwing or catching |  |  |  |  |  |  |
| Kicking or jumping |  |  |  |  |  |  |
| Applying a sudden or unexpected force including: Handling a live person or animal Applying uneven, fast or jerky forces during lifting, carrying, pushing or pulling Pushing or pulling objects that are hard move or stop e.g. a trolley |  |  |  |  |  |  |
| Exerting force while in a bent, twisted or awkward posture including: Supporting items with hands which are above shoulder height Moving items when legs are in an awkward posture, working with fingers pinched together or held wide apart Using a finger grip or pinch grip or an open handed grip |  |  |  |  |  |  |
| Exerting a force with the non-preferred hand |  |  |  |  |  |  |
| Needing to use two hands to operate a tool designed for one hand |  |  |  |  |  |  |
| The task can only be done for short periods of time |  |  |  |  |  |  |
| Two or more people need to be assigned to handle a heavy, awkward or bulky load |  |  |  |  |  |  |
| Workers report pain or significant discomfort during or after the task |  |  |  |  |  |  |
| Stronger workers assigned to do the task |  |  |  |  |  |  |
| Employees say the task is physically very strenuous or difficult to do |  |  |  |  |  |  |
| Workers think the task should be done by more than one person, or seek help as it requires high force |  |  |  |  |  |  |
| Step 4: Is there hand, arm or whole body vibration? If you answer yes in step 4, then the task requires further investigation |
| Driving for long periods |  |  |  |  |  |  |
| Driving on rough roads |  |  |  |  |  |  |
| Frequent use of hand powered tools or use for long periods |  |  |  |  |  |  |
| Using high grip forces or awkward postures when using power tools |  |  |  |  |  |  |
| Use of machines or tools where the manufacturer’s handbook warns of vibration |  |  |  |  |  |  |
| Workers being jolted or continuously shaken |  |  |  |  |  |  |
| Use of a vehicle or tool not suitable for the environment or task |  |  |  |  |  |  |

| PLANT - MAJOR – Summarise fixed / mobile plant or equipment: crushing plant / control room, excavator, FEL, dump truck, mobile jaw crusher, screendeck, forklift, watercart etc. |
| --- |
| Plant Name |  | Plant Identification No. |  |  |
| Model |  | Date of Manufacture |  |  |
| Has the relevant Certificate of Compliance (CoC) been received for new installation: Tick Y or N Box | Gas: | Y N | Electrical: | Y N | Plumbing: | Y N If No? Contact licensed installer to inspect and issue |

| The operator controls not located for ease of use Note: refer to the Code of Practice - Managing the Risks of Plant in the Workplace. |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| The emergency stops not located at the most likely places for use where work is being conducted |  |  |  |  |  |  |
| The controls not identified and labelled correctly |  |  |  |  |  |  |
| The emergency stops / pull wires not clearly marked |  |  |  |  |  |  |
| Lanyards not installed on conveyors to AS 1755 (Use MAQOHSC conveyor inspection checklist as a guide) |  |  |  |  |  |  |
| The green start buttons not shrouded or recessed? |  |  |  |  |  |  |
| No provisions available to lock out the plant and dissipate stored energy |  |  |  |  |  |  |
| Access platforms / ladders / stairs / handrails do not meet AS 1657 requirements? |  |  |  |  |  |  |
| No Residual Current Device (RCD) protection devices installed (Fixed plant only) |  |  |  |  |  |  |
| No adequate provision to service / routinely grease and oil the plant |  |  |  |  |  |  |
| No safe systems of work established for operating and maintenance of the plant |  |  |  |  |  |  |
| Arm, hand or fingers crushed, cut or amputated by rotating or moving parts on plant or machinery? |  |  |  |  |  |  |
| Hair or clothing caught by rotating moving parts of plant or machinery? |  |  |  |  |  |  |
| Contact with hot or cold parts on plant or machinery? |  |  |  |  |  |  |
| Being burnt by (hot / cold) solid, liquid or vapour escaping or being released from plant or machinery? |  |  |  |  |  |  |
| Radiation exposure from plant or machinery? |  |  |  |  |  |  |
| Being struck in the face / eye by ejected materials from plant or machinery? |  |  |  |  |  |  |
| Contact with exposed or damaged electrical wiring while operating or servicing / cleaning or repairing the plant or machinery? |  |  |  |  |  |  |
| Falling while working at height or from an elevated workplace on the plant or machinery? |  |  |  |  |  |  |
| Mobile plant rolling over during operation? e.g. no roll over protection (ROPS), no seat belt, etc. |  |  |  |  |  |  |
| Being struck by falling objects while operating mobile plant? e.g. no cabin, falling object protection (FOPS) |  |  |  |  |  |  |
| Being crushed by plant or machinery during operational or maintenance activities? |  |  |  |  |  |  |
| Workers untrained / not assessed for competency in plant and machinery operation |  |  |  |  |  |  |
| PLANT - MINOR – Summarise tools / equipment to be used: oxy welder or arc, hand operated cordless / electric or pneumatic powered tools, shovel, hammers etc. |
| Plant Names |  | Plant Identification No’s. |  |  |
| Models |  | Dates of Manufacture |  |  |
| Contact with compressed air? e.g. entering the eyes, ears or under the skin |  |  |  |  |  |  |
| Sharp edges or objects on plant? |  |  |  |  |  |  |
| Contact with unguarded rotating or moving blades or cutters? |  |  |  |  |  |  |
| Hands or fingers being squashed or crushed? |  |  |  |  |  |  |
| Being struck by material in the face or eye? e.g. slag chippings, metal filings, swarf, dust partials, etc. |  |  |  |  |  |  |
| Dropping tools or equipment onto legs or feet? |  |  |  |  |  |  |
| Being burnt from contact with hot or cold surfaces? |  |  |  |  |  |  |
| Electrocution from contact with exposed or damaged wiring of the plant? |  |  |  |  |  |  |
| Radiation exposure from the plant? e.g. arc / oxy welding Note: refer to the Code of Practice - Welding Processes. |  |  |  |  |  |  |
| Noise levels above 85db produced by the tools, plant, equipment or materials? |  |  |  |  |  |  |
| Workers untrained / not assessed for competency in the operation of plant? |  |  |  |  |  |  |

| HAZARDOUS CHEMICALS – Summarise chemicals: liquids, powders, aerosols, pellets, cleaners, solvents, glues, paints, sealers, oils, fuels and poisons |  |
| --- | --- |
| Note: for any asbestos related work, refer to the Code of Practice - How to Manage and Control Asbestos in the Workplace. |
| List any hazardous chemicals the worker may use or handle: |  |  |
|  |  |  |  | (obtained from Safety Data Sheet or label on container, drum or packaging) |  |
| Are there up to date Safety Data Sheets available for each chemical? | Yes |  | No |  |  |  |  |
| Are the chemical(s): |  | If no document Safety Data Sheets required and obtain from supplier / manufacturer |  |
| Skin or Digestive Irritant? |  |  | Toxic or Poisonous? |  | Corrosive / Caustic? |  | Classified as Dangerous Goods? |  |  |
| Eye or Respiratory Irritant |  |  | Flammable or Combustible? |  | Classified as Hazardous Substance? |  | Reactive or Explosive? |  |  |
| This section is for assessing risks associated with tasks involving the use of hazardous chemicals, a separate pre-purchase risk assessment will be required for all hazardous chemicals brought to site. |
| Incorrect labeling of chemical container? Note: refer to the Code of Practice - Labelling of Workplace Hazardous Chemicals. |  |  |  |  |  |  |
| Incorrect handling, storage or use of the chemical? (fire or explosion) Note: refer to MAQOHSC Hazardous Chemicals and Dangerous Substances Management Guide |  |  |  |  |  |  |
| Inhaling the fumes or odour of the chemical? |  |  |  |  |  |  |
| Skin contact with the chemical? |  |  |  |  |  |  |
| Splashed in the eyes by the chemical? |  |  |  |  |  |  |
| Accidentally ingesting (drink or swallow) the chemical? Note: refer to the Safety Data Sheet for information on the chemical. |  |  |  |  |  |  |
| Accidentally injecting the chemical into the workers body / under the skin? |  |  |  |  |  |  |
| Any other issues related to handling, storage or use of the chemical? Note: refer to MAQOHSC Hazardous Chemicals and Dangerous Substances Management Guide |  |  |  |  |  |  |

| OTHER PERSONS – Summarise: work that may place the health and safety of a third party at risk of injury or damage (other than an worker) |
| --- |
| Struck by an object ejected from the plant or equipment during operations? |  |  |  |  |  |  |
| Struck by a moving vehicle or mobile equipment? |  |  |  |  |  |  |
| Struck by a falling object that is being removed, dismantled, erected, positioned, lifted, carried or transported? |  |  |  |  |  |  |
| Property or vehicle damage from work being undertaken |  |  |  |  |  |  |
| Exposure to spray drift or residue from pesticides, herbicides, paints, adhesives, solvents, chemicals or any materials? |  |  |  |  |  |  |
| Exposure to dust or fumes caused by workplace operations? |  |  |  |  |  |  |
| Noise levels from work workplace operations? Note: refer to the Code of Practice - Managing Noise and Preventing Hearing Loss at Work. |  |  |  |  |  |  |
| A release of gas, power failure or disruption to underground services |  |  |  |  |  |  |
| Slipping, tripping or falling from a height or at ground level caused by work being undertaken? |  |  |  |  |  |  |
| Slipping, tripping or falling below ground level? Note: refer to the Code of Practice - Excavation Work. |  |  |  |  |  |  |

| ENVIRONMENTAL - Summarise any aspects of the work that may impact upon the environment |  |
| --- | --- |
| Dust escaping from the site boundaries? |  |  |  |  |  |  |
| Sediment escaping from the site boundaries and polluting adjoining lands, water courses and aquifers? |  |  |  |  |  |  |
| Waste water leaking into the storm water drainage system? |  |  |  |  |  |  |
| Polluting the land, adjoining waters or the storm water system with fuel or chemical spillages? |  |  |  |  |  |  |
| Soil erosion from water movement? |  |  |  |  |  |  |
| A negative impact on plants and animals from use of herbicides or pesticides |  |  |  |  |  |  |
| Waste material incorrectly disposed of? |  |  |  |  |  |  |
| Hazardous chemicals incorrectly disposed of? |  |  |  |  |  |  |

| Safe Operating Procedures (SOP) relevant to risk assessment. |
| --- |
| Safe Operating Procedure Name: |
| Recommendations on Methods for Ensuring Safe Work |
| Where a Safe Operating Procedure is developed, this Risk Assessment needs to be referenced within the document. |
| Action Plan |
| Action No | Action required | Responsibility | Completion Date | Review Date |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |
| 12 |  |  |  |  |
| 13 |  |  |  |  |
| 14 |  |  |  |  |
| 15 |  |  |  |  |
| 16 |  |  |  |  |
| 17 |  |  |  |  |
| 18 |  |  |  |  |
| 19 |  |  |  |  |
| 20 |  |  |  |  |
| 21 |  |  |  |  |
| 22 |  |  |  |  |
| 23 |  |  |  |  |
| 24 |  |  |  |  |
| 25 |  |  |  |  |
| 26 |  |  |  |  |
| 27 |  |  |  |  |
| 28 |  |  |  |  |
| 29 |  |  |  |  |
| 30 |  |  |  |  |
| 31 |  |  |  |  |
| 32 |  |  |  |  |
| 33 |  |  |  |  |
| 34 |  |  |  |  |
| 35 |  |  |  |  |
| 36 |  |  |  |  |
| 37 |  |  |  |  |
| 38 |  |  |  |  |
| 39 |  |  |  |  |
| 40 |  |  |  |  |